## Slide 1: Interconnection Networks: Routing
Prof. Natalie Enright Jerger

## Slide 2: Routing Overview
Discussion of topologies assumed ideal routing
In practice…
  Routing algorithms are not ideal
Goal: distribute traffic evenly among paths
  Avoid hot spots, contention
  More balanced  closer throughput is to ideal
Keep complexity in mind

## Slide 3: Routing Basics
Once topology is fixed
Routing algorithm determines path(s) from source to destination

## Slide 4: Routing Example
Some routing options:
  Greedy: shortest path
  Uniform random: randomly pick direction
  Adaptive: send packet in direction with lowest local channel load
Which gives best worst-case throughput?
0
1
2
3
4
5
6
7
Notes: What’s the point of this example – just to illustrate that counter-intuitive or something else?

## Slide 5: Routing Example (2)
Consider tornado traffic
  node i sends to i+3 mod 8
0
1
2
3
4
5
6
7

## Slide 6: Routing Example (3)
Greedy:
  All traffic moves counterclockwise
    Loads counterclockwise with 3 units of traffic
      Each node gets 1/3 throughput
    Clockwise channels are idle
Random:
  Clockwise channels become bottleneck
    Load of 5/2
      Half of traffic traverses 5 links in clockwise direction
      Gives throughput of 2/5

## Slide 7: Routing Example (4)
Adaptive:
  Perfect load balancing (some assumptions about implementation)
  Sends 5/8 of traffic over 3 links, sends 3/8 over 5 links
    Channel load is 15/8, throughput of 8/15
Note: worst case throughput just 1 metric designer might optimize

## Slide 8: Routing Algorithm Attributes
Types
  Deterministic, Oblivious, Adaptive
Number of destinations
  Unicast, Multicast, Broadcast?
Adaptivity
  Oblivious or Adaptive? Local or Global knowledge?
  Minimal or non-minimal?
Implementation
  Source or node routing?
  Table or circuit?

## Slide 9: Routing Deadlock
Each packet is occupying a link and waiting for a link
Without routing restrictions, a resource cycle can occur
  Leads to deadlock
A
B
D
C

## Slide 10: Deterministic
All messages from Source to Destination traverse the same path
Common example: Dimension Order Routing (DOR)
  Message traverses network dimension by dimension
  Aka XY routing
Cons:
  Eliminates any path diversity provided by topology
  Poor load balancing
Pros:
  Simple and inexpensive to implement
  Deadlock-free

## Slide 11: Dimension Order Routing: Cube networks
a.k.a X-Y Routing
  Traverse network dimension by dimension
  Can only turn to Y dimension after finished X

## Slide 12: Destination-Tag Routing: Butterfly Networks
Destination address
  Interpreted as an n-digit radix-k number
  Directly routes packet
Each digit selects the output port at each step
0
00
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
01
02
03
10
11
12
13
20
21
22
23
1
0
1
2-ary 3-fly

## Slide 13: Oblivious
Routing decisions are made without regard to network state
  Keeps algorithms simple
  Unable to adapt
Deterministic algorithms are a subset of oblivious
Notes: Start here

## Slide 14: Valiant’s Routing Algorithm
To route from s to d
  Randomly choose intermediate node d’
  Route from s to d’ and from d’ to d.
Randomizes any traffic pattern
  All patterns appear uniform random
  Balances network load
Non-minimal
Destroys locality
d’
d
s

## Slide 15: Minimal Oblivious
Valiant’s: Load balancing but significant increase in hop count
Minimal Oblivious: some load balancing, but use shortest paths
  d’ must lie within min quadrant
  6 options for d’
  Only 3 different paths
d
s

## Slide 16: Minimal Oblivious Routing on Fat Tree
Node labels (addr template)
  All nodes reachable from left terminals
Route from s to d
  Randomly selected, nearest common ancestor x of s and d
Route s to x then x to d
Example s = 1, d = 6
Construct route incrementally
  Randomly select output port
  Until addr template matches d
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
000X
001X
010X
011X
100X
101X
110X
111X
00XX
01XX
0XXX
A
0XXX
B
10XX
11XX
1XXX
A
1XXX
B
XXXX
A
XXXX
B
XXXX
C
XXXX
D
Notes: Start here…

## Slide 17: Oblivious Routing
Valiant’s and Minimal Oblivious
  Deadlock free
    When used in conjunction with X-Y routing
Randomly choose between X-Y and Y-X routes
  Oblivious but not deadlock free!

## Slide 18: Adaptive
Exploits path diversity
Uses network state to make routing decisions
  Buffer occupancies often used
  Coupled with flow control mechanism
Local information readily available
  Global information more costly to obtain
  Network state can change rapidly
  Use of local information can lead to non-optimal choices
Can be minimal or non-minimal

## Slide 19: Minimal Adaptive Routing
Local info can result in sub-optimal choices
d
s

## Slide 20: Non-minimal adaptive
Fully adaptive
Not restricted to take shortest path
Misrouting: directing packet along non-productive channel
  Priority given to productive output
  Some algorithms forbid U-turns
Livelock potential: traversing network without ever reaching destination
  Mechanism to guarantee forward progress
    Limit number of misroutings
Notes: Fbfly is an on-chip example with non-minimal routing

## Slide 21: Non-minimal routing example
Longer path with potentially lower latency
d
s
d
s
Livelock: continue routing in cycle

## Slide 22: Adaptive Routing Example
Should 3 route clockwise or counterclockwise to 7?
  5 is using all the capacity of link 5  6
Queue at node 5 will sense contention but not at node 3
Backpressure: allows nodes to indirectly sense congestion
  Queue in one node fills up, it will stop receiving flits
  Previous queue will fill up
If each queue holds 4 packets
  3 will send 8 packets before sensing congestion
0
1
2
3
4
5
6
7

## Slide 23: Congestion Information
Local
  Information about my neighbors only
  Implicitly available – I know how many downstream buffers are available (from flow control)
Global
  Information about all nodes
  Explicitly send status information
  Usually based on VC utilization or buffer occupancy
Timeliness

## Slide 24: Sending Congestion Information
Piggybacking
  Send congestion information along with packets
Extra side network
  More affordable in on-chip networks
  Broadcast
  Packetize
Aggregate or individual node

## Slide 25: Partially Adaptive Routing: Turn Model
DOR eliminates 4 turns
  N to E, N to W, S to E, S to W
  No adaptivity
Some adaptivity by removing 2 of 8 turns
  Remains deadlock free (like DOR)
West first
  Eliminates S to W and N to W
West first
Notes: All eliminate the North to West turn and then each eliminates one other turn to remove deadlock.

## Slide 26: Turn Model Routing
Negative first
  Eliminates E to S and N to W
North last
  Eliminates N to E and N to W
Odd-Even
  Eliminates 2 turns depending on if current node is in odd of even column
    Even column: E to N and N to W
    Odd column: E to S and S to W
  Deadlock free (disallow 180 turns)
  Better adaptivity
North last
Negative first

## Slide 27: Negative-First Routing Example
Limited or no adaptivity for certain source-destination pairs
(0,0)
(2,3)
(0,3)
(2,0)
Notes: animate?

## Slide 28: Turn Model Routing Deadlock
What about eliminating turns NW and WN?
Not a valid turn elimination
  Resource cycle results
Notes: animate?

## Slide 29: Adaptive Routing and Deadlock
Option 1: Eliminate turns that lead to deadlock
  Limits flexibility
Option 2: Allow all turns
  Give more flexibility
  Must use other mechanism to prevent deadlock
  Rely on flow control (later)
    Escape virtual channels

## Slide 30: Adaptive Routing: Other Topologies
Butterfly: no path diversity
  Can add extra stages for path diversity, adaptive routing
Fat tree (folded Clos)
  Similar to minimal oblivious
    But instead of randomly selecting path to least common ancestor
      Select adaptively (upstream)
      Message routed deterministically (downstream)

## Slide 31: Routing Implementation
Source tables
  Entire route specified at source
  Avoids per-hop routing latency
  Unable to adapt dynamically to network conditions
  Can specify multiple routes per destination
    Give fault tolerance and load balance
  Support reconfiguration (not specific to topology)

## Slide 32: Source Table Routing
Destination | Route 1 | Route 2
00 | X | X
10 | EX | EX
20 | EEX | EEX
01 | NX | NX
11 | NEX | ENX
21 | NEEX | ENEX
02 | NNX | NNX
12 | ENNX | NNEX
22 | EENNX | NNEEX
03 | NNNX | NNNX
13 | NENNX | ENNNX
23 | EENNNX | NNNEEX
(0,0)
Arbitrary length paths: storage overhead and packet overhead

## Slide 33: Node Tables
Store only next direction at each node
Smaller tables than source routing
Adds per-hop routing latency
Can adapt to network conditions
  Specify multiple possible outputs per destination
  Select randomly to improve load balancing

## Slide 34: Node Table Routing
Implements West-First Routing
Each node would have 1 row of table
  Max two possible output ports
To |  |  |  |  |  |  |  |  | 
From | 00 | 01 | 02 | 10 | 11 | 12 | 20 | 21 | 22
00 | X ¦- | N ¦ - | N ¦ - | E ¦ - | E ¦ N | E ¦ N | E ¦ - | E ¦ N | E ¦ N
01 | S ¦ - | X ¦ - | N ¦ - | E ¦ S | E ¦ - | E ¦ N | E ¦ S | E ¦ - | E ¦ N
02 | S ¦ - | S¦ - | X ¦ - | E ¦ S | E ¦ S | E ¦ - | E ¦ S | E ¦ S | E ¦ -
10 | W¦- | W¦- | W¦- | X ¦ - | N ¦ - | N ¦ - | E ¦ - | E ¦ N | E ¦ N
11 | W¦- | W¦- | W¦- | S ¦ - | X ¦ - | N ¦ - | E ¦ S | E ¦ - | E ¦ N
12 | W¦- | W¦- | W¦- | S ¦ - | S ¦ - | X ¦ - | E ¦ S | E ¦ S | E ¦ -
20 | W¦- | W¦- | W¦- | W¦- | W¦- | W¦- | X ¦ - | N ¦ - | N ¦ -
21 | W¦- | W¦- | W¦- | W¦- | W¦- | W¦- | S ¦ - | X ¦ - | N ¦ -
22 | W¦- | W¦- | W¦- | W¦- | W¦- | W¦- | S ¦ - | S ¦ - | X ¦ -
(1,0)
Notes: Illustrating both node table routing and an example of the turn model
(1,0) to (0,1) is N and W but can only go W because its west first.

## Slide 35: Implementation
Combinational circuits can be used
  Simple (e.g. DOR): low router overhead
  Specific to one topology and one routing algorithm
    Limits fault tolerance
Tables can be updated to reflect new configuration, network faults, etc

## Slide 36: Circuit Based
Next hop based on buffer occupancies
Or could implement simple DOR
Fixed w.r.t. topology
sx
x
sy
y
=0
=0
Route selection
Productive Direction Vector
+x
-x
+y
-y
exit
Queue lengths
Selected Direction Vector
+x
-x
+y
-y
exit
Notes: have the x and y deltas – check sign bit – positive or negative direction and check for zero.
loss of generality – specific to topology and routing algorithm

## Slide 37: Routing Algorithms: Implementation
Routing Algorithm | Source Routing | Combinational | Node Table
Deterministic |  |  | 
DOR | Yes | Yes | Yes
Oblivious |  |  | 
Valiant’s | Yes | Yes | Yes
Minimal | Yes | Yes | Yes
Adaptive | No | Yes | Yes

## Slide 38: Routing Summary
Latency paramount concern
  Minimal routing most common for NoC
  Non-minimal can avoid congestion and deliver low latency
To date: NoC research favors DOR for simplicity and deadlock freedom
  On-chip networks often lightly loaded
Only covered unicast routing
  Recent work on extending on-chip routing to support multicast