## Slide 1: ECE/CS 757: Advanced Computer Architecture II GPGPUs
Instructor:Mikko H Lipasti
Spring 2015
University of Wisconsin-Madison
Lecture notes based on slides created by John Shen, Mark Hill, David Wood, Guri Sohi, Jim Smith, Natalie Enright Jerger, Michel Dubois, Murali Annavaram, Per Stenström and probably others

## Slide 2: Lecture Outline
General Purpose Graphics Processing Unit (GPGPU)
Programming model overview (SPMD, BSP)
Hardware features (SIMT)
Programming environment
Reading: Chapter 1 of: H. Kim, R. Vuduc, S. Bahsorkhi, J. Choi, W.-M. Hwu, Chapter 1, “Performance Analysis and Tuning for General Purpose Graphics Processing Units (GPGPU),” Synthesis Lectures on Computer Architecture, http://www.morganclaypool.com/doi/abs/10.2200/S00451ED1V01Y201209CAC020

## Slide 3: GPGPU
“General purpose graphics processing unit”
  Harness GPU shader cores for general computation
  Poor name: oxymoron
History
  GPU shader cores provide increasing FP computation throughput
  Only accessible through graphic device driver (e.g. DirectX/OpenGL)
  Early 2000’s “hackers” learn to write programs
  Mid 2000’s Nvidia decides to create CUDA framework
  ATI follows with OpenCL
Compute Unified Device Architecture == CUDA
  Heavily-multithreaded multiprocessor, NCC-UMA (sort of)
  Software toolkit: C-like source/APIs => PTX binary

## Slide 4: Speedup of Applications
GeForce 8800 GTX vs. 2.2GHz Opteron 248
10 speedup in a kernel is typical, as long as the kernel can occupy enough parallel threads
25 to 400 speedup if the function’s data requirements and control flow suit the GPU and the application is optimized
Keep in mind that the speedup also reflects how suitable the CPU is for executing the kernel
© David Kirk/NVIDIA and Wen-mei W. Hwu, 2007
ECE 498AL, University of Illinois, Urbana-Champaign
Notes: All kernels have large numbers of simultaneously executing threads (ask me if you want to see details).
Most of the 10X kernels saturate memory bandwidth

## Slide 5: Single-Program Multiple-Data (SPMD)
CUDA integrated CPU + GPU application C program
  Serial C code executes on CPU
  Parallel Kernel C code executes on GPU thread blocks
CPU Serial Code
Grid 0
. . .
. . .
GPU Parallel Kernel
KernelA<<< nBlk, nTid >>>(args);
Grid 1
CPU Serial Code
GPU Parallel Kernel
KernelB<<< nBlk, nTid >>>(args);

## Slide 6: Grids and Blocks
A kernel is executed as a grid of thread blocks
  All threads share data memory space
A thread block is a batch of threads that can cooperate with each other by:
  Synchronizing their execution
    For hazard-free shared memory accesses
  Efficiently sharing data through a low latency shared memory
  Two threads from two different blocks cannot cooperate
Host
Kernel 1
Kernel 2
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Grid 2
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)
Courtesy: NVIDIA

## Slide 7: CUDA Thread Block
Programmer declares (Thread) Block:
  Block size 1 to 512 concurrent threads
  Block shape 1D, 2D, or 3D
  Block dimensions in threads
All threads in a Block execute the same thread program
Threads have thread id numbers within Block
Threads share data and synchronize while doing their share of the work
Thread program uses thread id to select work and address shared data
CUDA Thread Block
Thread Id #: 0 1 2 3 … m
Thread program
Courtesy: John Nickolls, NVIDIA

## Slide 8: GeForce-8 Series HW Overview
TPC
TPC
TPC
TPC
TPC
TPC
TEX
SM
SP
SP
SP
SP
SFU
SP
SP
SP
SP
SFU
Instruction Fetch/Dispatch
Instruction L1
Data L1
Texture Processor Cluster
Streaming Multiprocessor
SM
Shared Memory
Streaming Processor Array
…

## Slide 9: CUDA Processor Terminology
SPA
  Streaming Processor Array (variable across GeForce 8-series, 8 in GeForce8800)
TPC
  Texture Processor Cluster (2 SM + TEX)
SM
  Streaming Multiprocessor (8 SP)
  Multi-threaded processor core
  Fundamental processing unit for CUDA thread block
SP
  Streaming Processor
  Scalar ALU for a single CUDA thread

## Slide 10: Streaming Multiprocessor (SM)
Streaming Multiprocessor (SM)
  8 Streaming Processors (SP)
  2 Super Function Units (SFU)
Multi-threaded instruction dispatch
  1 to 512 threads active
  Shared instruction fetch per 32 threads
  Cover latency of texture/memory loads
20+ GFLOPS
16 KB shared memory
DRAM texture and memory access
SP
SP
SP
SP
SFU
SP
SP
SP
SP
SFU
Instruction Fetch/Dispatch
Instruction L1
Data L1
Streaming Multiprocessor
Shared Memory

## Slide 11: Thread Life Cycle in HW
Grid is launched on the SPA
Thread Blocks are serially distributed to all the SM’s
  Potentially >1 Thread Block per SM
Each SM launches Warps of Threads
  2 levels of parallelism
SM schedules and executes Warps that are ready to run
As Warps and Thread Blocks complete, resources are freed
  SPA can distribute more Thread Blocks
Host
Kernel 1
Kernel 2
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Grid 2
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)

## Slide 12: SM Executes Blocks
Threads are assigned to SMs in Block granularity
  Up to 8 Blocks to each SM as resource allows
  SM in G80 can take up to 768 threads
    Could be 256 (threads/block) * 3 blocks
    Or 128 (threads/block) * 6 blocks, etc.
Threads run concurrently
  SM assigns/maintains thread id #s
  SM manages/schedules thread execution
t0 t1 t2 … tm
Blocks
Texture L1
SP
Shared
Memory
MT IU
SP
Shared
Memory
MT IU
TF
L2
Memory
t0 t1 t2 … tm
Blocks
SM 1
SM 0

## Slide 13: Thread Scheduling/Execution
Each Thread Blocks is divided in 32-thread Warps
  This is an implementation decision, not part of the CUDA programming model
Warps are scheduling units in SM
If 3 blocks are assigned to an SM and each Block has 256 threads, how many Warps are there in an SM?
  Each Block is divided into 256/32 = 8 Warps
  There are 8 * 3 = 24 Warps
  At any point in time, only one of the 24 Warps will be selected for instruction fetch and execution.
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 1 Warps
Block 2 Warps
SP
SP
SP
SP
SFU
SP
SP
SP
SP
SFU
Instruction Fetch/Dispatch
Instruction L1
Data L1
Streaming Multiprocessor
Shared Memory

## Slide 14: SM Warp Scheduling
SM hardware implements zero-overhead Warp scheduling
  Warps whose next instruction has its operands ready for consumption are eligible for execution
  Eligible Warps are selected for execution on a prioritized scheduling policy
  All threads in a Warp execute the same instruction when selected
4 clock cycles needed to dispatch the same instruction for all threads in a Warp in G80
  If one global memory access is needed for every 4 instructions
  A minimal of 13 Warps are needed to fully tolerate 200-cycle memory latency
warp 8 instruction 11
SM multithreaded
Warp scheduler
warp 1 instruction 42
warp 3 instruction 95
warp 8 instruction 12
. . .
time
warp 3 instruction 96

## Slide 15: SM Execution Pipeline
Fetch one warp instruction/cycle
  from instruction L1 cache
  into any instruction buffer slot
Issue one “ready-to-go” warp instruction/cycle
  from any warp - instruction buffer slot
  operand scoreboarding used to prevent hazards
Issue selection based on round-robin/age of warp
SM broadcasts the same instruction to 32 Threads of a Warp
[From Synthesis Lecture]

## Slide 16: Scoreboarding
All register operands of all instructions in the Instruction Buffer are scoreboarded
  Status becomes ready after the needed values are deposited
  prevents hazards
  cleared instructions are eligible for issue
Decoupled Memory/Processor pipelines
  any thread can continue to issue instructions until scoreboarding prevents issue
  allows Memory/Processor ops to proceed in shadow of Memory/Processor ops

## Slide 17: CUDA Device Memory
Each thread can:
  R/W per-thread registers
  R/W per-thread local memory
  R/W per-block shared memory
  R/W per-grid global memory
  Read only per-grid constant memory
  Read only per-grid texture memory
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host
The host can R/W global, constant, and texture memories
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.

## Slide 18: Global, Constant, and Texture Memories (Long Latency Accesses)
Global memory
  Main means of communicating R/W Data between host and device
  Contents visible to all threads
Texture and Constant Memories
  Constants initialized by host
  Contents visible to all threads
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host
Courtesy: NDVIA

## Slide 19: Parallel Memory Sharing
Local Memory: per-thread
  Private per thread
  Auto variables, register spill
Shared Memory: per-Block
  Shared by threads of the same block
  Inter-thread communication
Global Memory: per-application
  Shared by all threads
  Inter-Grid communication
Thread
Local Memory
Grid 0
. . .
Global
Memory
. . .
Grid 1
Sequential
Grids
in Time
Block
Shared
Memory

## Slide 20: SM Operand Collector
Register File (RF)
  32 KB
  Provides 4 operands/clock
Operand collector requests RF reads, buffers values
  Resolves bank conflicts to RF banks
  RF banks are single-ported SRAM
[From Synthesis Lecture]

## Slide 21: Programmer View of Register File
There are 8192 registers in each SM in G80
  This is an implementation decision, not part of CUDA
  Registers are dynamically partitioned across all Blocks assigned to the SM
  Once assigned to a Block, the register is NOT accessible by threads in other Blocks
  Each thread in the same Block only access registers assigned to itself
4 blocks
3 blocks

## Slide 22: Constants
Immediate address constants
Indexed address constants
Constants stored in DRAM, and cached on chip
  L1 per SM
A constant value can be broadcast to all threads in a Warp
  Extremely efficient way of accessing a value that is common for all threads in a Block!
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU

## Slide 23: Shared Memory
Each SM has 16 KB of Shared Memory
  16 banks of 32bit words
CUDA uses Shared Memory as shared storage visible to all threads in a thread block
  read and write access
Not used explicitly for pixel shader programs
  we dislike pixels talking to each other 
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU

## Slide 24: Parallel Memory Architecture
In a parallel machine, many threads access memory
  Therefore, memory is divided into banks
  Essential to achieve high bandwidth
Each bank can service one address per cycle
  A memory can service as many simultaneous accesses as it has banks
Multiple simultaneous accesses to a bank result in a bank conflict
  Conflicting accesses are serialized
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0

## Slide 25: Bank Addressing Examples
No Bank Conflicts
  Linear addressing stride == 1
No Bank Conflicts
  Random 1:1 Permutation
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0

## Slide 26: Memory Coalescing
If thread accesses are to adjacent locations
  Coalescing logic merges them
  Results in many fewer (i.e. more efficient) memory accesses
If accesses are not coalescible
  Requests are serialized
  Warp takes longer to execute
  Less throughput, more energy consumpgion
[From Synthesis Lecture]

## Slide 27: Extended C
Declspecs
  global, device, shared, local, constant
Keywords
  threadIdx, blockIdx
Intrinsics
  __syncthreads
Runtime API
  Memory, symbol, execution management
Function launch
__device__ float filter[N];
__global__ void convolve (float *image) {
__shared__ float region[M];
...
region[threadIdx] = image[i];
__syncthreads()
...
image[j] = result;
}
// Allocate GPU memory
void *myimage = cudaMalloc(bytes)
// 100 blocks, 10 threads per block
convolve<<<100, 10>>> (myimage);

## Slide 28: Extended C
gcc / cl
G80 SASS
foo.sass
OCG
cudacc
EDG C/C++ frontend
Open64 Global Optimizer
GPU Assembly
foo.s
CPU Host Code
foo.cpp
Integrated source
(foo.cu)
Notes: TBD: Define SASS = SPA Assembly language.

## Slide 29: CUDA Programming Model: A Highly Multithreaded Coprocessor
The GPU is viewed as a compute device that:
  Is a coprocessor to the CPU or host
  Has its own DRAM (device memory)
  Runs many threads in parallel
Data-parallel portions of an application are executed on the device as kernels which run in parallel on many threads
Differences between GPU and CPU threads
  GPU threads are extremely lightweight
    Very little creation overhead
  GPU needs 1000s of threads for full efficiency
    Multi-core CPU needs only a few

## Slide 30: Thread Batching: Grids and Blocks
A kernel is executed as a grid of thread blocks
  All threads share data memory space
A thread block is a batch of threads that can cooperate with each other by:
  Synchronizing their execution
    For hazard-free shared memory accesses
  Efficiently sharing data through a low latency shared memory
Two threads from two different blocks cannot cooperate
Host
Kernel 1
Kernel 2
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Grid 2
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)
Courtesy: NDVIA

## Slide 31: Block and Thread IDs
Threads and blocks have IDs
  So each thread can decide what data to work on
  Block ID: 1D or 2D
  Thread ID: 1D, 2D, or 3D
Simplifies memory addressing when processing multidimensional data
  Image processing
  Solving PDEs on volumes
  …
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)
Courtesy: NDVIA

## Slide 32: A Simple Running Example Matrix Multiplication
A straightforward matrix multiplication example that illustrates the basic features of memory and thread management in CUDA programs
  Leave shared memory usage until later
  Local, register usage
  Thread ID usage
  Memory data transfer API between host and device

## Slide 33: Programming Model: Square Matrix Multiplication Example
P = M * N of size WIDTH x WIDTH
Without tiling:
  One thread handles one element of P
  M and N are loaded WIDTH times from global memory
M
N
P
WIDTH
WIDTH
WIDTH
WIDTH

## Slide 34: Step 1: Matrix Data Transfers
// Allocate the device memory where we will copy M to
Matrix Md;
Md.width = WIDTH;
Md.height = WIDTH;
Md.pitch = WIDTH;
int size = WIDTH * WIDTH * sizeof(float);
cudaMalloc((void**)&Md.elements, size);
// Copy M from the host to the device
cudaMemcpy(Md.elements, M.elements, size, cudaMemcpyHostToDevice);
// Read M from the device to the host into P
cudaMemcpy(P.elements, Md.elements, size, cudaMemcpyDeviceToHost);
...
// Free device memory
cudaFree(Md.elements);

## Slide 35: Step 2: Matrix Multiplication A Simple Host Code in C
// Matrix multiplication on the (CPU) host in double precision
// for simplicity, we will assume that all dimensions are equal
void MatrixMulOnHost(const Matrix M, const Matrix N, Matrix P)
{
for (int i = 0; i < M.height; ++i)
for (int j = 0; j < N.width; ++j) {
double sum = 0;
for (int k = 0; k < M.width; ++k) {
double a = M.elements[i * M.width + k];
double b = N.elements[k * N.width + j];
sum += a * b;
}
P.elements[i * N.width + j] = sum;
}
}

## Slide 36: Multiply Using One Thread Block
One Block of threads compute matrix P
  Each thread computes one element of P
Each thread
  Loads a row of matrix M
  Loads a column of matrix N
  Perform one multiply and addition for each pair of M and N elements
  Compute to off-chip memory access ratio close to 1:1 (not very high)
Size of matrix limited by the number of threads allowed in a thread block
Grid 1
Block 1
48
Thread
(2, 2)
BLOCK_SIZE
M
P
N

## Slide 37: Step 3: Matrix Multiplication Host-side Main Program Code
int main(void) {
// Allocate and initialize the matrices
Matrix M = AllocateMatrix(WIDTH, WIDTH, 1);
Matrix N = AllocateMatrix(WIDTH, WIDTH, 1);
Matrix P = AllocateMatrix(WIDTH, WIDTH, 0);
// M * N on the device
MatrixMulOnDevice(M, N, P);
// Free matrices
FreeMatrix(M);
FreeMatrix(N);
FreeMatrix(P);
return 0;
}

## Slide 38: Step 3: Matrix Multiplication Host-side code
// Matrix multiplication on the device
void MatrixMulOnDevice(const Matrix M, const Matrix N, Matrix P)
{
// Load M and N to the device
Matrix Md = AllocateDeviceMatrix(M);
CopyToDeviceMatrix(Md, M);
Matrix Nd = AllocateDeviceMatrix(N);
CopyToDeviceMatrix(Nd, N);
// Allocate P on the device
Matrix Pd = AllocateDeviceMatrix(P);
CopyToDeviceMatrix(Pd, P); // Clear memory

## Slide 39: Step 3: Matrix Multiplication Host-side Code (cont.)
// Setup the execution configuration
dim3 dimBlock(WIDTH, WIDTH);
dim3 dimGrid(1, 1);
// Launch the device computation threads!
MatrixMulKernel<<<dimGrid, dimBlock>>>(Md, Nd, Pd);
// Read P from the device
CopyFromDeviceMatrix(P, Pd);
// Free device matrices
FreeDeviceMatrix(Md);
FreeDeviceMatrix(Nd);
FreeDeviceMatrix(Pd);
}

## Slide 40: Step 4: Matrix Multiplication Device-side Kernel Function
// Matrix multiplication kernel – thread specification
__global__ void MatrixMulKernel(Matrix M, Matrix N, Matrix P)
{
// 2D Thread ID
int tx = threadIdx.x;
int ty = threadIdx.y;
// Pvalue is used to store the element of the matrix
// that is computed by the thread
float Pvalue = 0;

## Slide 41: Step 4: Matrix Multiplication Device-Side Kernel Function (cont.)
M
N
P
WIDTH
WIDTH
WIDTH
WIDTH
for (int k = 0; k < M.width; ++k)
{
float Melement = M.elements[ty * M.pitch + k];
float Nelement = Nd.elements[k * N.pitch + tx];
Pvalue += Melement * Nelement;
}
// Write the matrix to device memory;
// each thread writes one element
P.elements[ty * P.pitch + tx] = Pvalue;
}
ty
tx

## Slide 42: Step 5: Some Loose Ends
// Allocate a device matrix of same size as M.
Matrix AllocateDeviceMatrix(const Matrix M)
{
Matrix Mdevice = M;
int size = M.width * M.height * sizeof(float);
cudaMalloc((void**)&Mdevice.elements, size);
return Mdevice;
}
// Free a device matrix.
void FreeDeviceMatrix(Matrix M) {
cudaFree(M.elements);
}
void FreeMatrix(Matrix M) {
free(M.elements);
}

## Slide 43: Step 5: Some Loose Ends (cont.)
// Copy a host matrix to a device matrix.
void CopyToDeviceMatrix(Matrix Mdevice, const Matrix Mhost)
{
int size = Mhost.width * Mhost.height * sizeof(float);
cudaMemcpy(Mdevice.elements, Mhost.elements, size,
cudaMemcpyHostToDevice);
}
// Copy a device matrix to a host matrix.
void CopyFromDeviceMatrix(Matrix Mhost, const Matrix Mdevice)
{
int size = Mdevice.width * Mdevice.height * sizeof(float);
cudaMemcpy(Mhost.elements, Mdevice.elements, size,
cudaMemcpyDeviceToHost);
}

## Slide 44: Granularity Considerations
For Matrix Multiplication, should I use 8X8, 16X16 or 32X32 tiles?
  For 8X8, we have 64 threads per Block. Since each SM can take up to 768 threads, it can take up to 12 Blocks. However, each SM can only take up to 8 Blocks, only 512 threads will go into each SM!
  For 16X16, we have 256 threads per Block. Since each SM can take up to 768 threads, it can take up to 3 Blocks and achieve full capacity unless other resource considerations overrule.
  For 32X32, we have 1024 threads per Block. Not even one can fit into an SM!

## Slide 45: What’s new since G80?
More of everything
  Registers, threads, blocks, SPs per SM, SMs per chip, DPFP, DRAM bandwidth & capacity
Caches
  Shared L2 cache
  L1 cache vs. L1 scratchpad memory (configurable in ratios)
    L1 caches not coherent
Clock frequency: hasn’t changed much until Pascal gen (2016)
Fusion/APU organization: CPU & GPU on same die
  GPU L2 vs. CPU LLC may be shared or coherent (e.g. HSA)
  DRAM shared (kernel launch need not memcpy to GPU memory)
HBM/HBM2 – die-stacked DRAM with 2.5D interposer

## Slide 46: Lecture Outline
General Purpose Graphics Processing Unit (GPGPU)
Programming model overview (SPMD, BSP)
Hardware features (SIMT)
Programming environment
Reading: Chapter 1 of: H. Kim, R. Vuduc, S. Bahsorkhi, J. Choi, W.-M. Hwu, Chapter 1, “Performance Analysis and Tuning for General Purpose Graphics Processing Units (GPGPU),” Synthesis Lectures on Computer Architecture, http://www.morganclaypool.com/doi/abs/10.2200/S00451ED1V01Y201209CAC020