## Slide 1: ECE/CS 757: Advanced Computer Architecture II
Instructor:Mikko H Lipasti
Spring 2017
University of Wisconsin-Madison
Lecture notes based on slides created by John Shen, Mark Hill, David Wood, Guri Sohi, Jim Smith, Natalie Enright Jerger, Michel Dubois, Murali Annavaram, Per Stenström and probably others

## Slide 2: Lecture Outline
Introduction to Parallel Software
  Sources of parallelism
  Expressing parallelism
Programming Models
Major Abstractions
  Processes & threads
  Communication
  Synchronization
Shared Memory
  API description
  Implementation at ABI, ISA levels
  ISA support
Message Passing
  API description
  Implementation at ABI, ISA levels
  ISA support

## Slide 3: Parallel Software
Why is it so hard?
  Conscious mind is inherently sequential
  (sub-conscious mind is extremely parallel)
Identifying parallelism in the problem
Expressing parallelism to the hardware
Effectively utilizing parallel hardware
  Balancing work
  Coordinating work
Debugging parallel algorithms

## Slide 4: Finding Parallelism
Functional parallelism
  Car: {engine, brakes, entertain, nav, …}
  Game: {physics, logic, UI, render, …}
  Signal processing: {transform, filter, scaling, …}
Automatic extraction
  Decompose serial programs
Data parallelism
  Vector, matrix, db table, pixels, …
Request parallelism
  Web, shared database, telephony, …

## Slide 5: 1. Functional Parallelism
Functional parallelism
  Car: {engine, brakes, entertain, nav, …}
  Game: {physics, logic, UI, render, …}
  Signal processing: {transform, filter, scaling, …}
Relatively easy to identify and utilize
Provides small-scale parallelism
  3x-10x
Balancing stages/functions is difficult

## Slide 6: 2. Automatic Extraction
Automatic extraction
  Decompose serial programs
Works well for certain application types
  Regular control flow and memory accesses
Difficult to guarantee correctness in all cases
  Ambiguous memory dependences
  Requires speculation, support for recovery
Degree of parallelism
  Large (1000x) for easy cases
  Small (3x-10x) for difficult cases

## Slide 7: 3. Data Parallelism
Data parallelism
  Vector, matrix, db table, pixels, web pages,…
Large data => significant parallelism
Many ways to express parallelism
  Vector/SIMD
  Threads, processes, shared memory
  Message-passing
Challenges:
  Balancing & coordinating work
  Communication vs. computation at scale

## Slide 8: 4. Request Parallelism
Multiple users => significant parallelism
Challenges
  Synchronization, communication, balancing work
Web Browsing Users
Web Server(s)
Database Server(s)

## Slide 9: Balancing Work
Amdahl’s parallel phase f: all processors busy
If not perfectly balanced
  (1-f) term grows (f not fully parallel)
  Performance scaling suffers
  Manageable for data & request parallel apps
  Very difficult problem for other two:
    Functional parallelism
    Automatically extracted
Time
1
1-f
f

## Slide 10: Coordinating Work
Synchronization
  Some data somewhere is shared
  Coordinate/order updates and reads
  Otherwise  chaos
Traditionally: locks and mutual exclusion
  Hard to get right, even harder to tune for perf.
Research to reality: Transactional Memory
  Programmer: Declare potential conflict
  Hardware and/or software: speculate & check
  Commit or roll back and retry
  IBM, Intel, others, now support in HW

## Slide 11: Expressing Parallelism
SIMD – introduced by Cray-1 vector supercomputer
  MMX, SSE/SSE2/SSE3/SSE4, AVX at small scale
SPMD or SIMT – GPGPU model (later)
  All processors execute same program on disjoint data
  Loose synchronization vs. rigid lockstep of SIMD
MIMD – most general (this lecture)
  Each processor executes its own program
Expressed through standard interfaces
  API, ABI, ISA

## Slide 12: MP Interfaces
Levels of abstraction enable complex system designs (such as MP computers)
Fairly natural extensions of uniprocessor model
  Historical evolution

## Slide 13: Programming Models
High level paradigm for expressing an algorithm
  Examples:
    Functional
    Sequential, procedural
    Shared memory
    Message Passing
Embodied in high level languages that support concurrent execution
  Incorporated into HLL constructs
  Incorporated as libraries added to existing sequential language
Top level features:
  For conventional models – shared memory, message passing
  Multiple threads are conceptually visible to programmer
  Communication/synchronization are visible to programmer

## Slide 14: Application Programming Interface (API)
Interface where HLL programmer works
High level language plus libraries
  Individual libraries are sometimes referred to as an “API”
User level runtime software is often part of API implementation
  Executes procedures
  Manages user-level state
Examples:
  C and pthreads
  FORTRAN and MPI

## Slide 15: Application Binary Interface (ABI)
Program in API is compiled to ABI
Consists of:
  OS call interface
  User level instructions (part of ISA)

## Slide 16: Instruction Set Architecture (ISA)
Interface between hardware and software
  What the hardware implements
Architected state
  Registers
  Memory architecture
All instructions
  May include parallel (SIMD) operations
  Both non-privileged and privileged
Exceptions (traps, interrupts)

## Slide 17: Programming Model Elements
For both Shared Memory and Message Passing
Processes and threads
  Process: A shared address space and one or more threads of control
  Thread: A program sequencer and private address space
  Task: Less formal term – part of an overall job
  Created, terminated, scheduled, etc.
Communication
  Passing of data
Synchronization
  Communicating control information
  To assure reliable, deterministic communication

## Slide 18: sub-Outline
Shared Memory Model
  API-level Processes, Threads
  API-level Communication
  API-level Synchronization
Shared Memory Implementation
  Implementing Processes, Threads at ABI/ISA levels
  Implementing Communication at ABI/ISA levels
  Implementing Synchronization at ABI/ISA levels
In order of decreasing complexity:
synchronization, processes&threads, communication
Repeat the above for Message Passing

## Slide 19: Shared Memory
Flat shared memory or object heap
  Synchronization via memory variables enables reliable sharing
Single process
Multiple threads per process
  Private memory per thread
Typically built on shared memory hardware system

## Slide 20: Threads and Processes
Creation
  generic -- Fork
    (Unix forks a process, not a thread)
  pthread_create(….*thread_function….)
    creates new thread in current address space
Termination
  pthread_exit
    or terminates when thread_function terminates
  pthread_kill
    one thread can kill another

## Slide 21: Example
Unix process with two threads
  (PC and stack pointer actually part of ABI/ISA implementation)

## Slide 22: Shared Memory Communication
Reads and writes to shared variables via normal language (assignment) statements (e.g. assembly load/store)

## Slide 23: Shared Memory Synchronization
What really gives shared memory programming its structure
Usually explicit in shared memory model
  Through language constructs or API
Three major classes of synchronization
  Mutual exclusion (mutex)
  Point-to-point synchronization
  Rendezvous
Employed by application design patterns
  A general description or template for the solution to a commonly recurring software design problem.

## Slide 24: Mutual Exclusion (mutex)
Assures that only one thread at a time can access a code or data region
Usually done via locks
  One thread acquires the lock
  All other threads excluded until lock is released
Examples
  pthread_mutex_lock
  pthread_mutex_unlock
Two main application programming patterns
  Code locking
  Data locking

## Slide 25: Code Locking
Protect shared data by locking the code that accesses it
Also called a monitor pattern
Example of a critical section

## Slide 26: Data Locking
Protect shared data by locking data structure

## Slide 27: Data Locking
Preferred when data structures are read/written in combinations
Example:
  <thread 0>
  Lock(mutex_struct1)
  Lock(mutex_struct2)
  <access struct1>
  <access struct2>
  Unlock(mutex_data1)
  Unlock(mutex_data2)
  <thread 1>
  Lock(mutex_struct1)
  Lock(mutex_struct3)
  <access struct1>
  <access struct3>
  Unlock(mutex_data1)
  Unlock(mutex_data3)
  <thread 2>
  Lock(mutex_struct2)
  Lock(mutex_struct3)
  <access struct2>
  <access struct3>
  Unlock(mutex_data2)
  Unlock(mutex_data3)

## Slide 28: Deadlock
Data locking is prone to deadlock
  If locks are acquired in an unsafe order
Example:
Complexity
  Disciplined locking order must be maintained, else deadlock
  Also, composability problems
    Locking structures in a nest of called procedures
  <thread 0>
  Lock(mutex_data1)
  Lock(mutex_data2)
  <access data1>
  <access data2>
  Unlock(mutex_data1)
  Unlock(mutex_data2)
  <thread 1>
  Lock(mutex_data2)
  Lock(mutex_data1)
  <access data1>
  <access data2
  Unlock(mutex_data1)
  Unlock (mutex_data2)

## Slide 29: Efficiency
Lock Contention
  Causes threads to wait
Function of lock granularity
  Size of data structure or code that is being locked
Extreme Case:
  “One big lock” model for multithreaded OSes
  Easy to implement, but very inefficient
Finer granularity
  + Less contention
  - More locks, more locking code
  - perhaps more deadlock opportunities
Coarser granularity
  opposite +/- of above

## Slide 30: Point-to-Point Synchronization
One thread signals another that a condition holds
  Can be done via API routines
  Can be done via normal load/stores
Examples
  pthread_cond_signal
  pthread_cond_wait
    suspends thread if condition not true
Application program pattern
  Producer/Consumer
  <Producer> <Consumer>
  while (full ==1){}; wait while (full == 0){}; wait
  buffer = value; b = buffer;
  full = 1; full = 0;

## Slide 31: Rendezvous
Two or more cooperating threads must reach a program point before proceeding
Examples
  wait for another thread at a join point before proceeding
    example: pthread_join
  barrier synchronization
    many (or all) threads wait at a given point
Application program pattern
  Bulk synchronous programming pattern

## Slide 32: Bulk Synchronous Program Pattern
Thread 1
Thread 2
Thread N
. . .
Barrier
Compute
Communicate
Barrier
Compute
Communicate
Compute

## Slide 33: Summary: Synchronization and Patterns
mutex (mutual exclusion)
  code locking (monitors)
  data locking
point to point
  producer/consumer
rendezvous
  bulk synchronous

## Slide 34: sub-Outline
Shared Memory Model
  API-level Processes, Threads
  API-level Communication
  API-level Synchronization
Shared Memory Implementation
  Implementing Processes, Threads at ABI/ISA levels
  Implementing Communication at ABI/ISA levels
  Implementing Synchronization at ABI/ISA levels
In order of decreasing complexity:
synchronization, processes&threads, communication
Repeat the above for Message Passing

## Slide 35: API Implementation
Implemented at ABI and ISA level
  OS calls
  Runtime software
  Special instructions

## Slide 36: Processes and Threads
Three models
  OS processes
  OS threads
  User threads

## Slide 37: OS Processes
Thread == Process
Use OS fork to create processes
Use OS calls to set up shared address space (e.g. shmget)
OS manages processes (and threads) via run queue
Heavyweight thread switches
  OS call followed by:
  Switch address mappings
  Switch process-related tables
  Full register switch
Advantage
  Threads have protected private memory

## Slide 38: OS (Kernel) Threads
API pthread_create() maps to Linux clone()
  Allows multiple threads sharing memory address space
OS manages threads via run queue
Lighter weight thread switch
  Still requires OS call
  No need to switch address mappings
  OS switches architected register state and stack pointer

## Slide 39: User Threads
If memory mapping doesn’t change, why involve OS at all?
Runtime creates threads simply by allocating stack space
Runtime switches threads via user level instructions
  thread switch via jumps

## Slide 40: Implementing User Threads
Multiple kernel threads needed to get control of multiple hardware processors
Create kernel threads (OS schedules)
Create user threads that runtime schedules onto kernel threads

## Slide 41: Implementing User Threads

## Slide 42: Communication
Easy
Just map high level access to variables to ISA level loads and stores
Except for
Ordering of memory accesses -- later

## Slide 43: Synchronization
Implement locks and rendezvous (barriers)
Use loads and stores to implement lock:
  <thread 0> <thread 1>
  . . . .
  LAB1: Load R1, Lock LAB2: Load R1, Lock
  Branch LAB1 if R1==1 Branch LAB2 if R1==1
  Ldi R1, 1 Ldi R1,1
  Store Lock, R1 Store Lock, R1
  . .
  <critical section> <critical section>
  . .
  Ldi R1, 0 Ldi R1, 0
  Store Lock, R1 Store Lock, R1

## Slide 44: Lock Implementation
Does not work
Violates mutual exclusion if both threads attempt to lock at the same time
  In practice, may work most of the time…
  Leading to an unexplainable system hang every few days
  <thread 0> <thread 1>
  . . . .
  LAB1: Load R1, Lock LAB2: Load R1, Lock
  Branch LAB1 if R1==1 Branch LAB2 if R1==1
  Ldi R1, 1 Ldi R1,1
  Store Lock, R1 Store Lock, R1

## Slide 45: Lock Implementation
Reliable locking can be done with atomic read-modify-write instruction
Example: test&set
  read lock and write a one
  some ISAs also set CCs (test)
  <thread 1> <thread 2>
  . .
  LAB1: Test&Set R1, Lock LAB2: Test&Set R1, Lock
  Branch LAB1 if R1==1 Branch LAB2 if R1==1
  . .
  <critical section> <critical section>
  . .
  Reset Lock Reset Lock

## Slide 46: Atomic Read-Modify-Write
Many such instructions have been used in ISAs
More-or-less equivalent
  One can be used to implement the others
  Implement Fetch&Add with Test&Set:
  Test&Set(reg,lock) Fetch&Add(reg,value,sum) Swap(reg,opnd)
  reg ←mem(lock); reg ← mem(sum); temp←mem(opnd);
  mem(lock) ← 1; mem(sum)←mem(sum)+value; mem(opnd)← reg;
  reg ← temp
  try: Test&Set(lock);
  if lock == 1 go to try;
  reg ←mem(sum);
  mem(sum) ← reg+value;
  reset (lock);

## Slide 47: Sub-Atomic Locks
Use two instructions:
Load linked + Store conditional
  Load linked
    reads memory value
    sets special flag
    writes address to special global address register
  Flag cleared on
    operations that may violate atomicity
      (implementation-dependent)
      e.g., write to address by another processor
      can use cache coherence mechanisms (later)
    context switch
  Store conditional
    writes value if flag is set
    no-op if flag is clear
    sets CC indicating or failure

## Slide 48: Load-Linked Store-Conditional
Example: atomic swap (r4,mem(r1))
try: mov r3,r4 ;move exchange value
  ll r2,0(r1) ;load locked
  sc r3,0(r1) ;store conditional
  beqz r3,try ;if store fails
  mov r4,r2 ;load value to r4
RISC- style implementation
  Like many early RISC ideas, it seemed like a good idea at the time…
  register windows, delayed branches, special divide regs, etc.

## Slide 49: Lock Efficiency
Spin Locks
  tight loop until lock is acquired
  LAB1: Test&Set R1, Lock
  Branch LAB1 if R1==1
Inefficiencies:
  Memory/Interconnect resources, spinning on read/writes
  With a cache-based systems,
  writes  lots of coherence traffic
  Processor resource
    not executing useful instructions

## Slide 50: Efficient Lock Implementations
Test&Test&Set
  spin on check for unlock only, then try to lock
  with cache systems, all reads can be local
    no bus or external memory resources used
Test&Set with Backoff
  Insert delay between test&set operations (not too long)
  Each failed attempt  longer delay
  (Like ethernet collision avoidance)
  test_it: load reg, mem(lock)
  branch test_it if reg==1
  lock_it: test&set reg, mem(lock)
  branch test_it if reg==1

## Slide 51: Efficient Lock Implementations
Solutions just given save memory/interconnect resource
  Still waste processor resource
Use runtime to suspend waiting process
  Detect lock
  Place on wait queue
  Schedule another thread from run queue
  When lock is released move from wait queue to run queue

## Slide 52: Point-to-Point Synchronization
Can use normal variables as flags
  while (full ==1){} ;spin while (full == 0){} ;spin
  a = value; b = value;
  full = 1; full = 0;
Assumes sequential consistency (later)
  Using normal variables may cause problems with relaxed consistency models
May be better to use special opcodes for flag set/clear

## Slide 53: Barrier Synchronization
Uses a lock, a counter, and a flag
  lock for updating counter
  flag indicates all threads have incremented counter
  Barrier (bar_name, n) {
  Lock (bar_name.lock);
  if (bar_name.counter = 0) bar_name.flag = 0;
  mycount = bar_name.counter++;
  Unlock (bar_name.lock);
  if (mycount == n) {
  bar_name.counter = 0;
  bar_name.flag = 1;
  }
  else while(bar_name.flag = 0) {}; /* busy wait */
  }

## Slide 54: Scalable Barrier Synchronization
Single counter can be point of contention
Solution: use tree of locks
Example:
  threads 1,2,3,4,6 have completed

## Slide 55: Memory Ordering
Program Order
  Processor executes instructions in architected (PC) sequence
  or at least appears to
Loads and stores from a single processor execute in program order
  Program order must be satisfied
  It is part of the ISA
What about ordering of loads and stores from different processors

## Slide 56: Memory Ordering
Producer/Consumer example:
  T0: A=0; T1:
  Flag = 0;
    ....
    A=9; While (Flag==0){};
  Flag = 1; L2: if (A==0)...
Intuitively it is impossible for A to be 0 at L2
  But it can happen if the updates to memory are reordered by the memory system
In an MP system, memory ordering rules must be carefully defined and maintained

## Slide 57: Practical Implementation
Interconnection network with contention and buffering
  T0: A=0; T1:
  Flag = 0;
    ....
    A=9; While (Flag==0){};
  Flag = 1; if (A==0)...
T0
Interconnection Net
Memory
T1
A  9
A  9
Flag 1
Flag 1
Flag: 0
A: 0
Flag: 1
Flag: 1
A: 0

## Slide 58: Sequential Consistency
"A system is sequentially consistent if the result of any execution is the same as if the operations of all processors were executed in some sequential order and the operations of each individual processor appears in this sequence in the order specified by its program“ -- Leslie Lamport

## Slide 59: Memory Coherence
WRT individual memory locations, consistency is always maintained
  In producer/consumer examples, coherence is always maintained
Practically, memory coherence often reduces to cache coherence
  Cache coherence implementations to be discussed later
Summary
  Coherence is for a single memory location
  Consistency applies to apparent ordering of all memory locations
  Memory coherence and consistency are ISA concepts

## Slide 60: sub-Outline
Message Passing Model
  API-level Processes, Threads
  API-level Communication
  API-level Synchronization
Message Passing Implementation
  Implementing Processes, Threads at ABI/ISA levels
  Implementing Communication at ABI/ISA levels
  Implementing Synchronization at ABI/ISA levels

## Slide 61: Message Passing
Multiple processes (or threads)
Logical data partitioning
  No shared variables
Message Passing
  Threads of control communicate by sending and receiving messages
  May be implicit in language constructs
  More commonly explicit via API

## Slide 62: MPI –Message Passing Interface API
A widely used standard
  For a variety of distributed memory systems
    SMP Clusters, workstation clusters, MPPs, heterogeneous systems
Also works on Shared Memory MPs
  Easy to emulate distributed memory on shared memory HW
Can be used with a number of high level languages

## Slide 63: Processes and Threads
Lots of flexibility (advantage of message passing)
  1) Multiple threads sharing an address space
  2) Multiple processes sharing an address space
  3) Multiple processes with different address spaces
    and different OSes
1 and 2 are easily implemented on shared memory hardware (with single OS)
  Process and thread creation/management similar to shared memory
3 probably more common in practice
  Process creation often external to execution environment; e.g. shell script
  Hard for user process on one system to create process on another OS

## Slide 64: Process Management
Processes are given identifiers (PIds)
  “rank” in MPI
Process can acquire own PId
Operations can be conditional on PId
Message can be sent/received via PIds

## Slide 65: Process Management
Organize into groups
  For collective management and communication

## Slide 66: Communication and Synchronization
Combined in the message passing paradigm
  Synchronization of messages part of communication semantics
Point-to-point communication
  From one process to another
Collective communication
  Involves groups of processes
  e.g., broadcast

## Slide 67: Point to Point Communication
Use sends/receives
send(RecProc, SendBuf,…)
  RecProc is destination (wildcards may be used)
  SendBuf names buffer holding message to be sent
receive (SendProc, RecBuf,…)
  SendProc names sending process (wildcards may be used)
  RecBuf names buffer where message should be placed

## Slide 68: MPI Examples
MPI_Send(buffer,count,type,dest,tag,comm)
  buffer – address of data to be sent
  count – number of data items
  type – type of data items
  dest – rank of the receiving process
  tag – arbitrary programmer-defined identifier
  tag of send and receive must match
  comm – communicator number
MPI_Recv(buffer,count,type,source,tag,comm,status)
  buffer – address of data to be sent
  count – number of data items
  type – type of data items
  source – rank of the sending process; may be a wildcard
  tag – arbitrary programmer-defined identifier; may be a wildcard
  tag of send and receive must match
  comm – communicator number
  status – indicates source, tag, and number of bytes transferred

## Slide 69: Message Synchronization
After a send or receive is executed…
  Has message actually been sent? or received?
Asynchronous versus Synchronous
  Higher level concept
Blocking versus non-Blocking
  Lower level – depends on buffer implementation
    but is reflected up into the API

## Slide 70: Synchronous vs Asynchronous
Synchronous Send
  Stall until message has actually been received
  Implies a message acknowledgement from receiver to sender
Synchronous Receive
  Stall until message has actually been received
Asynchronous Send and Receive
  Sender and receiver can proceed regardless
  Returns request handle that can be tested for message receipt
  Request handle can be tested to see if message has been sent/received

## Slide 71: Asynchronous Send
MPI_Isend(buffer,count,type,dest,tag,comm,request)
  buffer – address of data to be sent
  count – number of data items
  type – type of data items
  dest – rank of the receiving process
  tag – arbitrary programmer-defined identifier
  tag of send and receive must match
  comm – communicator number
  request – a unique number that can be used later to test for completion (via Test or Wait)
Sending process is immediately free to do other work
Must test request handle before another message can be safely sent
  MPI_test – tests request handle # and returns status
  MPI_wait – blocks until request handle# is “done”

## Slide 72: Asynchronous Receive
MPI_Irecv(buffer,count,type,source,tag,comm,request)
  buffer – address of data to be sent
  count – number of data items
  type – type of data items
  source – rank of the sending process; may be a wildcard
  tag – arbitrary programmer-defined identifier; may be a wildcard
  tag of send and receive must match
  comm – communicator number
  request – a unique number that can be used later to test for completion
Receiving process does not wait for message
Must test request handle before message is known to be in buffer
  MPI_test – tests request handle # and returns status
  MPI_wait – blocks until request handle# is “done”

## Slide 73: MPI Example: Comm. Around a Ring
  int main(argc,argv)
  int argc;
  char *argv[];
  {
  int numprocs, rank, next, prev, buf[2], tag1=1, tag2=2;
  MPI_Request reqs[4];
  MPI_Status stats[4];
  MPI_Init(&argc,&argv);
  MPI_Comm_size(MPI_COMM_WORLD, &numprocs);
  MPI_Comm_rank(MPI_COMM_WORLD, &rank);
  prev = rank-1;
  next = rank+1;
  if (rank == 0) prev = numprocs - 1;
  if (rank == (numprocs - 1)) next = 0;
  MPI_Irecv(&buf[0], 1, MPI_INT, prev, tag1, MPI_COMM_WORLD, &reqs[0]);
  MPI_Irecv(&buf[1], 1, MPI_INT, next, tag2, MPI_COMM_WORLD, &reqs[1]);
  MPI_Isend(&rank, 1, MPI_INT, prev, tag2, MPI_COMM_WORLD, &reqs[2]);
  MPI_Isend(&rank, 1, MPI_INT, next, tag1, MPI_COMM_WORLD, &reqs[3]);
  MPI_Waitall(4, reqs, stats);
  MPI_Finalize();
  }

## Slide 74: Deadlock
Blocking communications may deadlock
Requires careful (safe) ordering of sends/receives
Also depends on buffering
  System buffering may not eliminate deadlock, just postpone it
  <Process 0> <Process 1>
  Send(Process1, Message); Receive (Process0, Message);
  Receive(Process1, Message); Send (Process0, Message);
  <Process 0> <Process 1>
  Send(Process1, Message); Send(Process0, Message);
  Receive(Process1, Message); Receive(Process0, Message);

## Slide 75: Collective Communications
Involve all processes within a communicator
Blocking
MPI_Barrier (comm)
  Barrier synchronization
MPI_Bcast (*buffer,count,datatype,root,comm)
  Broadcasts from process of rank “root” to all other processes
MPI_Scatter (*sendbuf,sendcnt,sendtype,*recvbuf, ...... recvcnt,recvtype,root,comm)
  Sends different messages to each process in a group
MPI_Gather (*sendbuf,sendcnt,sendtype,*recvbuf, ...... recvcount,recvtype,root,comm)
  Gathers different messages from each process in a group
Also reductions

## Slide 76: Communicators and Groups
Define collections of processes that may communicate
  Often specified in message argument
  MPI_COMM_WORLD – predefined communicator that contains all processes

## Slide 77: Broadcast Example
98
Process 0
SendBuf
98
Process 0
RcvBuf
98
Process 1
RcvBuf
98
Process 2
RcvBuf
98
Process 3
RcvBuf

## Slide 78: Scatter Example
55
Process 0
SendBuf
23
Process 0
RcvBuf
37
Process 1
RcvBuf
42
Process 2
RcvBuf
55
Process 3
RcvBuf
42
37
23

## Slide 79: Gather Example
55
Process 0
RcvBuf
23
Process 0
SendBuf
37
Process 1
SendBuf
42
Process 2
SendBuf
55
Process 3
Sendbuf
42
37
23

## Slide 80: Message Passing Implementation
At the ABI and ISA level
  No special support (beyond that needed for shared memory)
  Most of the implementation is in the runtime
    user-level libraries
  Makes message passing relatively portable
Three implementation models (given earlier)
  1) Multiple threads sharing an address space
  2) Multiple processes sharing an address space
  3) Multiple processes with non-shared address space
    and different OSes

## Slide 81: Multiple Threads Sharing Address Space
Runtime manages buffering and tracks communication
  Communication via normal loads and stores using shared memory
Example: Send/Receive
  Send calls runtime, runtime posts availability of message in runtime-managed table
  Receive calls runtime, runtime checks table, finds message
  Runtime copies data from send buffer to store buffer via load/stores
Fast/Efficient Implementation
  May even be advantageous over shared memory paradigm
    considering portability, software engineering aspects
  Can use runtime thread scheduling
  Problem with protecting private memories and runtime data area

## Slide 82: Multiple Processes Sharing Address Space
Similar to multiple threads sharing address space
Would rely on kernel scheduling
May offer more memory protection
  With intermediate runtime buffering
  User processes can not access others’ private memory

## Slide 83: Multiple Processes with Non-Shared Address Space
Most common implementation
Communicate via networking hardware
Send/receive to runtime
  Runtime converts to OS (network) calls
Relatively high overhead
  Most HPC systems use special low-latency, high-bandwidth networks
  Buffering in receiver’s runtime space may save some overhead for receive (doesn’t require OS call)

## Slide 84: At the ISA Level: Shared Memory
Multiple processors
Architected shared virtual memory
Architected Synchronization instructions
Architected Cache Coherence
Architected Memory Consistency

## Slide 85: At the ISA Level: Message Passing
Multiple processors
Shared or non-shared real memory (multi-computers)
Limited ISA support (if any)
  An advantage of distributed memory systems --Just connect a bunch of small computers
  Some implementations may use shared memory managed by runtime

## Slide 86: Lecture Summary
Introduction to Parallel Software
Programming Models
Major Abstractions
  Processes & threads
  Communication
  Synchronization
Shared Memory
  API description
  Implementation at ABI, ISA levels
  ISA support
Message Passing
  API description
  Implementation at ABI, ISA levels
  ISA support
Not covered: openmp, intel tbb, CUDA (later), etc.