## Slide 1: Interconnection Networks: Router Microarchitecture
Prof. Natalie Enright Jerger

## Slide 2: Introduction
Topology: connectivity
Routing: paths
Flow control: resource allocation
Router microarchitecture: implementation of routing, flow control and router pipeline
  Impacts per-hop delay and energy

## Slide 3: Router Microarchitecture Overview
Focus on microarchitecture of Virtual Channel (VC) router
  Router complexity increase with bandwidth demands
  Simple routers built when high throughput is not needed
    Wormhole flow control, unpipelined, limited buffers

## Slide 4: Virtual Channel Router
Route Computation
VC Allocator
Switch Allocator
Input buffers
VC 1
VC 2
VC 3
VC 4
Input buffers
VC 1
VC 2
VC 3
VC 4
Crossbar switch
Input 5
Input 1
Output 5
Output 1
Credits In
Credits Out

## Slide 5: Router Components
Input buffers, route computation logic, virtual channel allocator, switch allocator, crossbar switch
Most OCN routers are input buffered
  Use single-ported memories
Buffer store flits for duration in router
  Contrast with processor pipeline that latches between stages

## Slide 6: Baseline Router Pipeline
Logical stages
  Fit into physical stages depending on frequency
Canonical 5-stage pipeline
  BW: Buffer Write
  RC: Routing computation
  VA: Virtual Channel Allocation
  SA: Switch Allocation
  ST: Switch Traversal
  LT: Link Traversal
BW
RC
VA
SA
ST
LT

## Slide 7: Baseline Router Pipeline (2)
Routing computation performed once per packet
Virtual channel allocated once per packet
Body and tail flits inherit this info from head flit
BW
RC
VA
SA
ST
LT
BW
BW
BW
SA
ST
LT
SA
ST
LT
SA
ST
LT
Head
Body 1
Body 2
Tail
1
2
3
4
5
6
7
8
9

## Slide 8: Router Pipeline Performance
Baseline (no load) delay
Ideally, only pay link delay
Techniques to reduce pipeline stages

## Slide 9: Pipeline Optimizations: Lookahead Routing
At current router perform routing computation for next router
  Overlap with BW
  Precomputing route allows flits to compete for VCs immediately after BW
  RC decodes route header
  Routing computation needed at next hop
    Can be computed in parallel with VA
BW
RC
VA
SA
ST
LT

## Slide 10: Atomic Modules and Dependencies in Router
Dependence between output of one module and input of another
  Determine critical path through router
  Cannot bid for switch port until routing performed
Decode + Routing
Switch Arbitration
Crossbar Traversal
Wormhole Router
Decode + Routing
Switch Arbitration
Crossbar Traversal
Virtual Channel Router
VC Allocation
Decode + Routing
Speculative Switch Arbitration
Crossbar Traversal
Speculative Virtual Channel Router
VC Allocation

## Slide 11: Atomic Modules
Some components of router cannot be easily pipelined
Example: pipeline VC allocation
  Grants might not be correctly reflected before next allocation
Separable allocator: many wires connecting input/output stages
  Require latches if pipelined

## Slide 12: Pipeline Optimizations: Speculation
Assume that Virtual Channel Allocation stage will be successful
  Valid under low to moderate loads
Entire VA and SA in parallel
If VA unsuccessful (no virtual channel returned)
  Must repeat VA/SA in next cycle
Prioritize non-speculative requests
BW
RC
VA
SA
ST
LT

## Slide 13: Pipeline Optimizations: Bypassing
When no flits in input buffer
  Speculatively enter ST
  On port conflict, speculation aborted
  In the first stage, a free VC is allocated, next routing is performed and the crossbar is setup
VA
RC
Setup
ST
LT

## Slide 14: Pipeline Bypassing
No buffered flits when A arrives
Inject
N
S
E
W
Eject
N
S
E
W
1b
1a
Lookahead Routing Computation
1
2
A
Virtual Channel Allocation

## Slide 15: Speculation
Inject
N
S
E
W
Eject
N
S
E
W
1b
1a
Lookahead Routing Computation
1
1c
1
1b
1c
Virtual Channel Allocation
Switch Allocation
2a
2b
3
4
Port conflict detected
3
A succeeds in VA but fails in SA, retry SA
B
A

## Slide 16: Buffer Organization
Single buffer per input
Multiple fixed length queues per physical channel
Physical channels
Virtual channels
Notes: Also multiple variable length queues

## Slide 17: Buffer Organization
Multiple variable length queues
  Multiple VCs share a large buffer
  Each VC must have minimum 1 flit buffer
    Prevent deadlock
  More complex circuitry
VC 0
tail
head
VC 1
tail
head

## Slide 18: Buffer Organization
Many shallow VCs?
Few deep VCs?
More VCs ease HOL blocking
  More complex VC allocator
Light traffic
  Many shallow VCs – underutilized
Heavy traffic
  Few deep VCs – less efficient, packets blocked due to lack of VCs

## Slide 19: Switch Organization
Heart of datapath
  Switches bits from input to output
High frequency crossbar designs challenging
Crossbar composed for many multiplexers
  Common in low-frequency router designs
Long wires: repeater insertion
i00
i10
i20
i30
i40
o0
sel0
o1
sel1
o2
sel2
o3
sel3
o4
sel4

## Slide 20: Switch Organization: Crosspoint
Area and power scale at O((pw)2)
  p: number of ports (function of topology)
  w: port width in bits (determines phit/flit size and impacts packet energy and delay)
Inject
N
S
E
W
Eject
N
S
E
W
w columns
w rows

## Slide 21: Crossbar speedup
Increase internal switch bandwidth
Simplifies allocation or gives better performance with a simple allocator
  More inputs to select from  higher probability each output port will be matched (used) each cycle
10:5 crossbar
5:10 crossbar
10:10 crossbar

## Slide 22: Switch Microarchitecture: No Speedup
Routing Control
and
Arbitration Unit
Physical
channel
Input buffers
Link
Control
...
MUX
DEMUX
Physical
channel
Physical
channel
CrossBar
Physical
channel
Input buffers
Link
Control
...
MUX
DEMUX

## Slide 23: Switch Microarchitecture: Speedup
Routing Control
and
Arbitration Unit
Physical
channel
Input buffers
Link
Control
...
MUX
DEMUX
Physical
channel
Physical
channel
CrossBar
Physical
channel
Input buffers
Link
Control
...
MUX
DEMUX
Switch
input
speedup

## Slide 24: Switch Microarchitecture: Speedup
Output buffers
Routing Control
and
Arbitration Unit
Input buffers
Link
Control
Physical
channel
...
Physical
channel
...
DEMUX
MUX
DEMUX
MUX
Input buffers
Link
Control
Physical
channel
...
DEMUX
MUX
Output buffers
Physical
channel
...
DEMUX
MUX
CrossBar
Switch
input & output
speedup

## Slide 25: Crossbar Dimension Slicing
Crossbar area and power grow with O((pw)2)
Replace 1 5x5 crossbar with 2 3x3 crossbars
Suited to DOR
  Traffic mostly stays within 1 dimension
Inject
E-in
W-in
E-out
W-out
N-in
S-in
N-out
S-out
Eject
Notes: Ports and width

## Slide 26: Arbiters and Allocators
Allocator matches N requests to M resources
Arbiter matches N requests to 1 resource
Resources are VCs (for virtual channel routers) and crossbar switch ports.

## Slide 27: Arbiters and Allocators (2)
Virtual-channel allocator (VA)
  Resolves contention for output virtual channels
  Grants them to input virtual channels
Switch allocator (SA) that grants crossbar switch ports to input virtual channels
Allocator/arbiter that delivers high matching probability translates to higher network throughput.
  Must also be fast and/or able to be pipelined
VC allocation typically determines cycle time

## Slide 28: Fairness
Intuitively, a fair arbiter is one that provides equal service to different requesters
Weak fairness: Every request is eventually served
Strong fairness: Requesters will be served equally often
FIFO Fairness: Requesters are served in the order they make their requests

## Slide 29: Locally Fair Example
R3 receives 4 times the bandwidth as r0, even though individual arbiters provide strong fairness
A0
A1
A2
r3
Destination
1.0
0.5
0.5
r2
0.25
0.25
0.125
0.125
r1
r0

## Slide 30: Round Robin Arbiter
Last request serviced given lowest priority
Generate the next priority vector from current grant vector
If no requests, priority is unchanged
Exhibits fairness

## Slide 31: Round Robin (2)
Gi granted, next cycle Pi+1 high
Grant 0
Grant 1
Grant 2
Next priority 0
Next priority 1
Next priority 2
Priority 0
Priority 1
Priority 2

## Slide 32: Weighted Round-Robin Arbiter
Disable request if input has already reached its quota
Weight
Count = 0
Arbiter
p
d
r
preset
g

## Slide 33: Matrix Arbiter
Least recently served priority scheme
Triangular array of state bits wij for j < i
  Bit wij indicates request i takes priority over j
  Each time request k granted, clears all bits in row k and sets all bits in column k
Good for small number of inputs
Fast, inexpensive and provides strong fairness

## Slide 34: Matrix Arbiter (2)
Request 0
01
02
10
Request 1
20
21
12
Grant 0
Disable 2
Disable 1
Disable 0
Request 2
Grant 1
Grant 2

## Slide 35: Matrix Arbiter (3)
When a request is asserted
  AND-ed with the state bits in its row to disable any lower priority requests
  Outputs of AND gates in column are OR-ed together to generate disable signal
Request 0
01
02
10
Request 1
20
21
12
Grant 0
Disable 2
Disable 1
Disable 0
Request 2
Grant 1
Grant 2
1
0
0

## Slide 36: Matrix Arbiter (4)
If Request 2 granted
  Clear row 2
  Set column 2
wij
gj
gi
w2,0
g0
g2
1
0
1
0
w0,2
g2
g0
0
1
0
1

## Slide 37: Matrix Arbiter Example
Request 0
01
02
10
Request 1
20
01
01
Grant 0
Disable 2
Disable 1
Disable 0
Request 2
Grant 1
Grant 2
0
0
0
1
1
1
A1
A2
B1
C1
C2
0
1
2
Bit [1,0] = 1, Bit [2,0] = 1  1 and 2 have priority over 0
Bit [2,1] = 1  2 has priority over 1
C1 (Req 2) granted

## Slide 38: Matrix Arbiter Example (2)
Request 0
01
02
10
Request 1
20
01
01
Grant 0
Disable 2
Disable 1
Disable 0
Request 2
Grant 1
Grant 2
0
1
1
1
0
0
A1
A2
B1
C2
Set column 2, clear row 2
Bit [1,0] = 1, Bit [1,2] = 1  Req 1 has priority over 0 and 2
Grant B1 (Req 1)

## Slide 39: Matrix Arbiter Example (3)
Request 0
01
02
10
Request 1
20
01
01
Grant 0
Disable 2
Disable 1
Disable 0
Request 2
Grant 1
Grant 2
1
1
0
0
0
1
A1
A2
C2
Set column 1, clear row 1
Bit [0,1] = 1, Bit [0,2] = 1  Req 0 has priority over 1 and 2
Grant A1 (Req 0)

## Slide 40: Matrix Arbiter Example (4)
Request 0
01
02
10
Request 1
20
01
01
Grant 0
Disable 2
Disable 1
Disable 0
Request 2
Grant 1
Grant 2
0
0
0
1
1
1
A2
C2
Set column 0, clear row 0
Bit [2,0] = 1, Bit [2,1] = 1  Req 2 has priority over 0 and 1
Grant C2 (Req 2)

## Slide 41: Matrix Arbiter Example (5)
Request 0
01
02
10
Request 1
20
01
01
Grant 0
Disable 2
Disable 1
Disable 0
Request 2
Grant 1
Grant 2
0
1
1
1
0
0
A2
Set column 2, clear row 2
Grant Request A2

## Slide 42: Allocators
Arbiter assigns a single resource to one of a group of requesters
Allocator performs a matching between a group of resources and a group of requestors
  Each of which may request one or more resources
3 rules
  A grant can be asserted only if the corresponding request is asserted
  At most one grant for each input (requester) may be asserted
  At most one grant for each output (resource) can be asserted

## Slide 43: Allocation Example
Request Matrix, R =
Both G1 an G2 satisfy rules but G2 is more desirable
  All three resources assigned to inputs
  Maximum matching: solution containing maximum possible number of assignments
1 | 1 | 1
1 | 1 | 0
1 | 0 | 0
0 | 1 | 0
1 | 0 | 0
0 | 1 | 0
0 | 0 | 0
0 | 0 | 0
G1 =
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
0 | 0 | 0
G2 =
Notes: Rows = inputs, columns = output

## Slide 44: Exact Algorithms
Allocation problem can be represented as a bipartite graph
Exact algorithms not feasible in time budget of router
Useful to compare a new heuristic against

## Slide 45: Augmenting Paths Algorithm
Start with sub-optimal matching of the bipartite graph
Construct a directed residual graph
  If an edge is in the current matching, M, it points from its output to input
Now augmenting path is found
  Any directed path through the residual graph from an unmatched input to an unmatched output
  Matching is updated using this path

## Slide 46: Augmenting Paths Example
1 | 1 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 0
R =
0
0
1
1
2
2
3
3
4
4
5
5

## Slide 47: Augmenting Paths Example
1 | 1 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 0
R =
0
0
1
1
2
2
3
3
4
4
5
5

## Slide 48: Augmenting Paths Example
1 | 1 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 0
R =
0
0
1
1
2
2
3
3
4
4
5
5

## Slide 49: Augmenting Paths Example
1 | 1 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 0
R =
0
0
1
1
2
2
3
3
4
4
5
5

## Slide 50: Augmenting Paths Example
1 | 1 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 0
R =
0
0
1
1
2
2
3
3
4
4
5
5

## Slide 51: Augmenting Paths Example
1 | 1 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 0
R =
0
0
1
1
2
2
3
3
4
4
5
5

## Slide 52: Augmenting Paths Example
1 | 1 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 0
R =
0
0
1
1
2
2
3
3
4
4
5
5

## Slide 53: Wavefront Allocator
Arbitrates among requests for inputs and outputs simultaneously
Row and column tokens granted to diagonal group of cells
If a cell is requesting a resource, it will consume row and column tokens
  Request is granted
Cells that cannot use tokens
  Pass row tokens to right and column tokens down

## Slide 54: Wavefront Allocator Example
p0
p1
p2
p3
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
A requesting Resources 0, 1 ,2
B requesting Resources 0, 1
C requesting Resource 0
D requesting Resources 0, 2
Tokens inserted at P0
Entry [0,0] receives grant, consumes token
Remaining tokens pass down and right
[3,2] receives 2 tokens and is granted

## Slide 55: Wavefront Allocator Example
p0
p1
p2
p3
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
[1,1] receives 2 tokens and granted
All wavefronts propagated
Notes: Inherently sequential process, does not scale to large number of resources/requestors

## Slide 56: Separable Allocator
Need for pipelineable allocators
Allocator composed of arbiters
  Arbiter chooses one out of N requests to a single resource
Separable switch allocator
  First stage: select single request at each input port
  Second stage: selects single request for each output port

## Slide 57: Separable Allocator
A 3:4 allocator
First stage: 3:1 – ensures only one grant for each input
Second stage: 4:1 – only one grant asserted for each output
3:1 arbiter
3:1 arbiter
3:1 arbiter
3:1 arbiter
4:1 arbiter
4:1 arbiter
4:1 arbiter
Requestor 1 requesting resource A
Requestor 1 requesting resource C
Requestor 4 requesting resource A
Resource A granted to Requestor 1
Resource A granted to Requestor 2
Resource A granted to Requestor 3
Resource A granted to Requestor 4
Resource C granted to Requestor 1
Resource C granted to Requestor 4
Resource C granted to Requestor 2
Resource C granted to Requestor 3

## Slide 58: Separable Allocator Example
Input-first allocator
4 requestors, 3 resources
Arbitrate locally among requests
  Local winners passed to second stage
3:1 arbiter
3:1 arbiter
3:1 arbiter
3:1 arbiter
4:1 arbiter
4:1 arbiter
4:1 arbiter
A
B
C
A
B
A
A
C
Requestor 1 wins A
Requestor 4 wins C

## Slide 59: Adaptive Routing & Allocator Design
Deterministic routing
  Single output port
  Switch allocator bids for output port
Adaptive routing
  Returns multiple candidate output ports
    Switch allocator can bid for all ports
    Granted port must match VC granted
  Return single output port
    Reroute if packet fails VC allocation

## Slide 60: Speculative VC Router
Non-speculative switch requests must have higher priority than speculative ones
  Two parallel switch allocators
    1 for speculative
    1 for non-speculative
    From output, choose non-speculative over speculative
  Possible for flit to succeed in speculative switch allocation but fail in virtual channel allocation
    Done in parallel
    Speculation incorrect
      Switch reservation is wasted
  Body and Tail flits: non-speculative switch requests
    Do not perform VC allocation  inherit VC from head flit

## Slide 61: Microarchitecture Summary
Ties together topological, routing and flow control design decisions
Pipelined for fast cycle times
Area and power constraints important in NoC design space