## Slide 1: ECE/CS 757: Advanced Computer Architecture II SIMD
Instructor:Mikko H Lipasti
Spring 2017
University of Wisconsin-Madison
Lecture notes based on slides created by John Shen, Mark Hill, David Wood, Guri Sohi, Jim Smith, Natalie Enright Jerger, Michel Dubois, Murali Annavaram, Per Stenström and probably others

## Slide 2: SIMD & MPP Readings
Read: [20] C. Hughes, “Single-Instruction Multiple-Data Execution,” Synthesis Lectures on Computer Architecture, http://www.morganclaypool.com/doi/abs/10.2200/S00647ED1V01Y201505CAC032
Review: [21] Steven L. Scott, Synchronization and Communication in the T3E Multiprocessor, Proceedings of International Conference on Architectural Support for Programming Languages and Operating Systems, pages 26-36, October 1996.

## Slide 3: Lecture Outline
SIMD introduction
Automatic Parallelization for SIMD machines
Vector Architectures
  Cray-1 case study

## Slide 4: SIMD vs. Alternatives
From [Hughes, SIMD Synthesis Lecture]

## Slide 5: SIMD vs. Superscalar
From [Hughes, SIMD Synthesis Lecture]

## Slide 6: Multithreaded vs. Multicore
From [Hughes, SIMD Synthesis Lecture]

## Slide 7: SIMD Efficiency
From [Hughes, SIMD Synthesis Lecture]
Amdahl’s Law…

## Slide 8: SIMD History
Vector machines, supercomputing
  Illiac IV, CDC Star-100, TI ASC,
  Cray-1: properly architected (by Cray-2 gen)
Incremental adoption in microprocessors
  Intel Pentium MMX: vectors of bytes
  Subsequently: SSEx/AVX-y, now AVX-512
  Also SPARC, PowerPC, ARM, …
  Improperly architected…
  Also GPUs from AMD/ATI and Nvidia (later)

## Slide 9: Register Overlays
From [Hughes, SIMD Synthesis Lecture]

## Slide 10: SIMD Challenges
Remainders
  Fixed vector length, software has to fix up
  Properly architected: VL is supported in HW
Control flow deviation
  Conditional behavior in loop body
  Properly architected: vector masks
Memory access
  Alignment restrictions
  Virtual memory, page faults (completion masks)
  Irregular accesses: properly architected gather/scatter
Dependence analysis (next)

## Slide 11: Lecture Outline
SIMD introduction
Automatic Parallelization for SIMD machines
Vector Architectures
  Cray-1 case study

## Slide 12: Automatic Parallelization
Start with sequential programming model
Let the compiler attempt to find parallelism
  It can be done…
  We will look at one of the success stories
Commonly used for SIMD computing – vectorization
  Useful for MIMD systems, also -- concurrentization
Often done with FORTRAN
  But, some success can be achieved with C
  (Compiler address disambiguation is more difficult with C)

## Slide 13: Automatic Parallelization
Consider operations on arrays of data
  do I=1,N
    A(I,J) = B(I,J) + C(I,J)
  end do
  Operations along one dimension involve vectors
Loop level parallelism
  Do all – all loop iterations are independent
    Completely parallel
  Do across – some dependence across loop iterations
    Partly parallel
  A(I,J) = A(I-1,J) + C(I,J) * B(I,J)

## Slide 14: Data Dependence
Independence  Parallelism
  OR, dependence inhibits parallelism
  S1: A=B+C
  S2: D=A+2
  S3: A=E+F
True Dependence (RAW):
  S1  S2
Antidependence (WAR):
  S2 - S3
Output Dependence (WAW):
  S1 o S3

## Slide 15: Data Dependence Applied to Loops
Similar relationships for loops
  But consider iterations
  do I=1,2
  S1: A(I)=B(I)+C(I)
  S2: D(I)=A(I)
  end do
S1 = S2
  Dependence involving A, but on same loop iteration

## Slide 16: Data Dependence Applied to Loops
S1 < S2
  do I=1,2
  S1: A(I)=B(I)+C(I)
  S2: D(I)=A(I-1)
  end do
  Dependence involving A, but read occurs on next loop iteration
  Loop carried dependence
S2 -< S1
  Antidependence involving A, write occurs on next loop iteration
  do I=1,2
  S1: A(I)=B(I)+C(I)
  S2: D(I)=A(I+1)
  end do

## Slide 17: Loop Carried Dependence
  Definition
    do I = 1, N
  S1: X(f(i)) = F(...)
  S2: A = X(g(i)) ...
  end do
  S1  S2 : is loop-carried
    if there exist i1, i2 where
  1 i1 < i2  N and f(i1) = g(i2 )
  If f and g can be arbitrary functions, the problem is essentially unsolvable.
  However, if (for example)
  f(i) = c*I + j and g(i) = d*I + k
  there are methods for detecting dependence.

## Slide 18: Loop Carried Dependences
GCD test
  do I = 1, N
  S1: X(c*I + j ) = F(...)
  S2: A = X(d*I + k) ...
  end do
  f(x) = g(y) if c*I + j = d*I + k
  This has a solution iff gcd(c, d ) | k- j
Example
  A(2*I) =
  = A(2*I +1)
  GCD(2,2) does not divide 1 - 0
The GCD test is of limited use because it is very conservative
  often gcd(c,d) = 1
  X(4i+1) = F(X(5i+2))
Other, more complex tests have been developed
  e.g. Banerjee's Inequality, polyhedral analysis

## Slide 19: Vector Code Generation
In a vector architecture, a vector instruction performs identical operations on vectors of data
Generally, the vector operations are independent
  A common exception is reductions (horizontal ops)
In general, to vectorize:
  There should be no cycles in the dependence graph
  Dependence flows should be downward
   some rearranging of code may be needed.

## Slide 20: Vector Code Generation: Example
do I = 1, N
S1: A(I) = B(I)
S2: C(I) = A(I) + B(I)
S3: E(I) = C(I+1)
end do
Construct dependence graph
S1:

S2:
-
S3:
Vectorizes (after re-ordering S2: and S3: due to antidependence)
S1: A(I:N) = B(I:N)
S3: E(I:N) = C(2:N+1)
S2: C(I:N) = A(I:N) + B(I:N)

## Slide 21: Multiple Processors (Concurrentization)
Often used on outer loops
Example
do I = 1, N
do J = 2, N
S1: A(I,J) = B(I,J) + C(I,J)
S2: C(I,J) = D(I,J)/2
S3: E(I,J) = A(I,J-1)**2 + E(I,J-1)
end do
end do
Data Dependences & Directions
S1 =, < S3
S1 =, = S2
S3 =, < S3
Observations
  All dependence directions for I loop are =
   Iterations of the I loop can be scheduled in parallel

## Slide 22: Scheduling
Data Parallel Programming Model
  SPMD (single program, multiple data)
Compiler can pre-schedule:
  Processor 1 executes 1st N/P iterations,
  Processor 2 executes next N/P iterations
  Processor P executes last N/P iterations
  Pre-scheduling is effective if execution time is nearly identical for each iteration
Self-scheduling is often used:
  If each iteration is large
  Time varies from iteration to iteration
    iterations are placed in a "work queue”
    a processor that is idle, or becomes idle takes the next block of work from the queue (critical section)

## Slide 23: Code Generation with Dependences
  do I = 2, N
S1: A(I) = B(I) + C(I)
S2: C(I) = D(I) * 2
S3: E(I) = C(I) + A(I-1)
  end do
Data Dependences & Directions
S1 -= S2
S1 < S3
S2 = S3
Parallel Code on N-1 Processors
S1: A(I) = B(I) + C(I)
signal(I)
S2: C(I) = D(I) * 2
if (I > 2) wait(I-1)
S3: E(I) = C(I) + A(I-1)
Observation
  Weak data-dependence tests may add unnecessary synchronization.
  Good dependence testing crucial for high performance

## Slide 24: Reducing Synchronization
do I = 1, N
S1: A(I) = B(I) + C(I)
S2: D(I) = A(I) * 2
S3: SUM = SUM + A(I)
end do
Parallel Code: Version 1
do I = p, N, P
S1: A(I) = B(I) + C(I)
S2: D(I) = A(I) * 2
if (I > 1) wait(I-1)
S3: SUM = SUM + A(I)
signal(I)
end do

## Slide 25: Reducing Synchronization, contd.
Parallel Code: Version 2
  SUMX(p) = 0
  do I = p, N, P
S1: A(I) = B(I) + C(I)
S2: D(I) = A(I) * 2
S3: SUMX(p) = SUMX(p) + A(I)
end do
barrier synchronize
add partial sums
Not always safe (bit-equivalent): why?

## Slide 26: Vectorization vs Concurrentization
When a system is a vector MP, when should vector/concurrent code be generated?
do J = 1,N
do I = 1,N
S1: A(I,J+1) = B(I,J) + C(I,J)
S2: D(I,J) = A(I,J) * 2
end do
end do
Parallel & Vector Code: Version 1
doacross J = 1,N
S1: A(1:N,J+1) = B(1:N,J)+C(1:N,J)
signal(J)
if (J > 1) wait (J-1)
S2: D(1:N,J) = A(1:N,J) * 2
end do

## Slide 27: Vectorization vs Concurrentization
Parallel & Vector Code: Version 2
Vectorize on J, but non-unit stride memory access
(assuming Fortran Column Major storage order)
doall I = 1,N
S1: A(I,2:N+1) = B(I,1:N) + C(I,1:N)
S2: D(I,1:N) = A(I,1:N) * 2
end do
Need support for gather/scatter

## Slide 28: Summary
Vectorizing compilers have been a success
Dependence analysis is critical to any auto-parallelizing scheme
  Software (static) disambiguation
  C pointers are especially difficult
Can also be used for improving performance of sequential programs
  Loop interchange
  Fusion
  Etc.

## Slide 29: Aside: Thread-Level Speculation
Add hardware to resolve difficult concurrentization problems
Memory dependences
  Speculate independence
  Track references (cache versions, r/w bits, similar to TM)
  Roll back on violations
Thread/task generation
  Dynamic task generation/spawn (Multiscalar)
References
  Gurindar S. Sohi , Scott E. Breach , T. N. Vijaykumar, Multiscalar processors, Proceedings of the 22nd annual international symposium on Computer architecture, p.414-425, June 22-24, 1995
  J. Steffan , T Mowry, The Potential for Using Thread-Level Data Speculation to Facilitate Automatic Parallelization, Proceedings of the 4th International Symposium on High-Performance Computer Architecture, p.2, January 31-February 04, 1998

## Slide 30: Cray-1 Architecture
Circa 1976
80 MHz clock
  When high performance mainframes were 20 MHz
Scalar instruction set
  16/32 bit instruction sizes
    Otherwise conventional RISC
  8 S register (64-bits)
  8 A registers (24-bits)
In-order pipeline
  Issue in order
  Can complete out of order (no precise traps)

## Slide 31: Cray-1 Vector ISA
8 vector registers
  64 elements
  64 bits per element (word length)
  Vector length (VL) register
RISC format
  Vi  Vj OP Vk
  Vi  mem(Aj, disp)
Conditionals via vector mask (VM) register
  VM  Vi pred Vj
  Vi  V2 conditional on VM

## Slide 32: Vector Example
Do 10 i=1,looplength
a(i) = b(i) * x + c(i)
10 continue
A1  looplength .initial values:
A2  address(a) .for the arrays
A3  address(b) .
A4  address(c) .
A5  0 .index value
A6  64 .max hardware VL
S1  x .scalar x in register S1
VL  A1 .set VL – performs mod function
.
BrC done, A1<=0 .branch if nothing to do
more: V3  A4,A5 .load c indexed by A5 – addr mode not in Cray-1
V1  A3,A5 .load b indexed by A5
V2  V1 * S1 .vector times scalar
V4  V2 + V3 .add in c
A2,A5  V4 .store to a indexed by A5
A7  VL .read actual VL
A1  A1 – A7 .remaining iteration count
A5  A5 + A7 .increment index value
VL  A6 . set VL for next iteration
BrC more, A1>0 .branch if more work
done:

## Slide 33: Compare with Scalar
Do 10 i=1,looplength
a(i) = b(i) * x + c(i)
10 continue
2 loads
1 store
2 FP
1 branch
1 index increment (at least)
1 loop count increment
total -- 8 instructions per iteration
4-wide superscalar => up to 1 FP op per cycle
vector, with chaining => up to 2 FP ops per cycle (assuming mem b/w)
Also, in a CMOS microprocessor would save a lot of energy
.

## Slide 34: Vector Conditional Loop
do 80 i = 1,looplen
if (a(i).eq.b(i)) then
c(i) = a(i) + e(i)
endif
80 continue
V1  A1 .load a(i)
V2  A2 .load b(i)
VM  V1 == V2 .compare a and b; result to VM
V3  A3; VM .load e(i) under mask
V4  V1 + V3; VM .add under mask
A4  V4; VM .store to c(i) under mask

## Slide 35: Vector Conditional Loop
Gather/Scatter Method (used in later Cray machines)
do 80 i = 1,looplen
if (a(i).eq.b(i)) then
c(i) = a(i) + e(i)
endif
80 continue
V1  A1 .load a(i)
V2  A2 .load b(i)
VM  V1 == V2 .compare a and b; result to VM
V5  IOTA(VM) .form index set
VL  pop(VM) .find new VL (population count)
V6  A1, V5 .gather a(i) values
V3  A3, V5 .gather e(i) values
V4  V6 + V3 .add a and e
A4,V11  V4 .scatter sum into c(i)

## Slide 36: Lecture Summary
SIMD introduction
Automatic Parallelization
Vector Architectures
  Cray-1 case study