## Slide 1: PInterNet Where multi core simulation becomes network aware
Team Members: Simon Xu, Preyas Shah, Rahul Nayar, Fan Wu

## Slide 2: Outline
Motivation
Design Overview
ZSim- Overview, Infrastructure and Modifications
Router- Micro-architecture and Implementation
BookSim - Overview, Infrastructure and Modifications
Results
Open Issues/Future Work
Conclusions
A vote of thanks – Cheers!!!!

## Slide 3: Motivation
Issues with Multi Core Simulation
Sequential – extremely slow
Scale poorly or not accurate
ZSIM
  1500 MIPS for Simple Cores, 300 for OOO cores
  Within15% accurate of real systems
Awesome, What's the catch?
There are many, but we pick this one:
Does not support NOC – remains future work since 2013
Can We do something about it?
This is why 757 has project component
PInterNet

## Slide 4: Design Overview
Accelerator Processing Unit
Processing Units
16 partitions
8 Cores/partition
128 Cores
Memory
8KB 2 way L1 I$
16KB 2 way L1 D$
Network
128KB 4 way L2 shared
4x4 Mesh
5 links
2 stage Router
RISCV cores
Weak Consistency Model

## Slide 5: ZSim – why do we love it and hate it?
What makes it faster?
  Instruction Driven Timing Models – dynamic binary translation
  Bound and Weave Phase
  Virtualized system view
Which kind of cores does it support?
  Beefy Core – Westemere microarch
  Wimpy Core – single IPC core model
Bound Phase
  One host thread per simulated core - || execution
  Event Trace for misses beyond trace hierarchy
Weave Phase
  Event queue simulation in-order
  Divide system into domains – each domain has own priority queue
    Faster
    Report domain crossings
Limitation on fine-grained messaging
Weave phase is network congestion oblivious

## Slide 6: ZSim – Bound and Weave Phase
Synchronize all the Threads
Bound Phase Execution
Update all Memory reference in a Queue
Weave Phase Execution
Synchronize all the Threads
Dequeue all Memory references and apply latency Panelties

## Slide 7: ZSim Modeling overview
Courtesy: ZSim Authors
Not Using It

## Slide 8: ZSim – current configuration
Beefy OOO Core
Thread Scheduling
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
Partitioned Memory
Issues with this modeling:
  Oblivious of Bound and Weave Phase
  Unaware of Network Congestion
  No phase wise tracking of all Out Of Partition accesses
  Constant penalty to all Out Of Partition accesses

## Slide 9: ZSim Modifications
Beefy OOO Core
Thread Scheduling
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
8 Wimpy core + L1$
Partitioned Memory
Issues:
Oblivious of Bound and Weave Phase
Unaware of Network Congestion
No phase wise tracking of all OOP accesses
Constant penalty to all OOP accesses
Modifications:
Keep track of all OOPs in Bound Phase
Sync Barries between Bound and Weave
BookSim to calculate latency penalty based on OOPs of last bound phase
Latency penalization to Cores in Weave Phase
L2$ mimic in Weave Phase

## Slide 10: PInterNet Router Overview
Design Goal
Easy to design :p
High Performance
  Low latency/high throughput
  Optimize for real workloads
Synthesizable and fast
Highly Parameterizable
  Chisel has good parameterization support
Chisel (Scala-based)
FIRRTL
Verilog
Synopsys Design Compiler
Unit test Verification
Performance Eval
Peek-Poke Tester
Testing Framework

## Slide 11: PInterNet Router Specs
Mesh Network (5-in-5-out)
Cut-Through
Credit Based Flow Control
XY-Routing
Virtual Channel
two-cycle Latency
Fully Parameterizable
Hit 1GHz Freq @ ARM 55nm
Flit Structure (assuming 32-bit bus)

## Slide 12
N
S
E
W
PInterNet Router Microarchitecture
Local
N
S
E
W
Local

## Slide 13
N
S
E
W
PInterNet Router Microarchitecture
Local
N
S
E
W
Local
Input Units
(Routing Calculation,
1st-level Arbitration
Data Buffering)
Distributed
VC Allocator
Switch Allocator
(2nd-level Arbitration,
VC assignment,
Routing Resource Allocation,
Deadlock Prevention)
Output Units
(Credit Stats,
Credit/Channel Release signaling,
Buffering)
Hierarchical arbitration: helps relieve timing constraints
Static routing and RR-policy achieves deadlock prevention
Distributed allocators: simplify the design while maintain good throughput

## Slide 14: Performance Evaluation
Lightly loaded—close to ideal
Heavily loaded—exponential growth
What do real-life workloads suggest?
VertexCover:
<5 OOPs/100cycles/router
WordCount:
<1 OOPs/100cycles/router
PageRank (Peak):
~25 OOPs/100cycles/router
Optimize for common cases and let uncommon cases fail gracefully

## Slide 15: One Step Further – A Single-Cycle Router
Non-intrusive bypassing route
Light-weight Speculation Logic
Zero-cycle penalty on mis-speculation

## Slide 16: Performance Evaluation (2)
2 Virtual Channels
128-bit bus
VA speculation
~-20%
~perf of 4VCs
~perf of design without speculation

## Slide 17: BookSim Overview
Cycle-accurate network simulator for demonstration purposes
Supports various networks, including ring, mesh, and torus
Packets are generated randomly given injection rate
Does not allow the use of custom trace

## Slide 18: Zsim & BookSim Integration
Problem 1: BookSim does not allow the injection of a custom trace
Solution: Replace the random packet generation logic with one that reads the trace file generated by Zsim
Problem 2: We need a way to integrate BookSim and Zsim.
Solution: Create a shared booksimapi.hpp header that provides API to be called from Zsim. Through the API, Zsim can supply trace file to BookSim and control its execution.
Problem 3: For read access, Zsim only issues a read request; In real situations, there is also a read response.
Solution: In BookSim, upon the delivery of a read request, a read response is injected a few cycles later.

## Slide 19: BookSim Router Implementation
We modified the canonical 5-stage router in BookSim to mimic the 2-stage router in our RTL design.

## Slide 20: Results
Workloads used for testing the infrastructure
  Histogram
  Wordcount
  VertexCover
  PageRank

## Slide 21: Workload
Histogram:
  Make no OOP load/store access
  Most of the accesses are focused on the same partition
  Used to check the change in simulation time for PInterNet for interconnect is not accessed
Wordcount:
  Moderate amount of OOP load access, no OOP stores
  Used this to check the initial setup of our PInternet, and gain confidence if our zsim + bookism infrastructure that is working
Vertexcover:
  Large amount of OOP load access with no stores
  Testing our PInternet setup
Pagerank
  Large OOP load and store access comes from this workload
  OOP load and store access are distributed across different partition
  Use this workload to do the uniform testing of the mesh interconnect system

## Slide 22: Workload Characteristics
Notes: Histogram
Make no OOP load/store access
Most of the access are focused on the same core/partition
Since we have used the bookism for mesh interconnect setup, this workload will be convince us that we are not increasing the simulation time in PinterNet when no OOP access is made
Wordcount
Moderate amount of OOP load access no OOP stores
Used this to check the initial setup of our Pinternet, and gain confidence if our zsim + bookism infrastructure that is working
Vertexcover
Large amount of OOP load access with no stores
Wordcount
Moderate amount of OOP load access no OOP stores
Used this to check the initial setup of our Pinternet, and gain confidence if our zsim + bookism infrastructure that is working
Pagerank
Most OOP load and store access comes from this workload
OOP load and store access are distributed across different partition
We use this workload to do the uniform testing of the mesh interconnect system

## Slide 23: Simulation time with/without booksim
*Values extrapolated for PageRank and VertexCover

## Slide 24: OOP per Cycle

## Slide 25: PageRank Characteristics
Total OOP load/Store access distributed uniformly among all the 16 partitions
Few cases the OOP load/store is larger than other cases, this information is useful to check for the possible corner cases in the router implementation
OOP load traffic low during the initial phase but becomes larger after 43k phase number (1 PhaseLength = 100000)
OOP Store traffic is the opposite, higher traffic during the initial phase but is reduced and more uniform around 43k phase number

## Slide 26: PageRank Traffic Pattern

## Slide 27: Page Rank Traffic Pattern

## Slide 28: Traffic Pattern Case Study - PageRank
Why?
  Identify possible congestion in the 4x4 mesh networks
  Possible optimizations in router implementation
  Our network implements uses credit based flow control, for max throughput optimal buffer size needs to be set, this is done by studying the traffic pattern
  Identify better network topologies for different workloads
Difference Between Load & Store Access Patterns of same Partition
Difference Store Access Patterns of Different Partition
Difference Load Access Patterns of Different Partition

## Slide 29: Future Work
RTL vs PInterNet Correlation for accuracy
Make PInterNet generic
  Support other topologies
  Integration with generic version of ZSim
Run Time improvements
  Find correct region of interest and have cut off based system
  Parallelize the execution of Zsim+bookism
  Identify the ideal phaselength to further improve on the simulation time without compromising on the accuracy.
Pin tool crashing for more than 35000 phases(with Booksim) – debug pending
For performance evaluation, we need to try and reduce the delay further to set the workloads to be less than 10 oops/100 cycles
A more aggressive VC allocation implementation for the router
Congestion identification for Network
  Apply various traffic patterns
  More workload analysis

## Slide 30: Conclusion
Contribution
  A network congestion aware simulator for many core systems
  A router design and implementation for multi core system
Learnings
  Understanding a many core design
  ZSim - implementation and principles of fast multi core simulators
  Intricacies and tradeoffs of Network Router implementation
  BookSim simulator
  Shared environment development for simulators integration

## Slide 31: A note of thanks
Prof. Mikko Lipasti
  For guidance of network and router design and simulators
Members of Vertical Research Group
  William, Vijay and Vinay
  For making us understand design and help with infrastructure bring up

## Slide 32: Back Up Slides

## Slide 33: Page Rank Traffic Pattern
2
3
4
6
7
8
9
10
11
12
13
14
15
0
1
5
Node Degree: 2,3,4
Plot the traffic pattern of partition 0,1 and 2

## Slide 34: Page Rank Traffic Pattern
Partition-0 make most of the store request to the furthest partition, partition-15
Partition-0 load pattern request is not similar to partition-0 store pattern request

## Slide 35: Page Rank Traffic Pattern

## Slide 36: Page Rank Traffic Pattern

## Slide 37: Future Work
RTL vs PInterNet Correlation for accuracy
Run Time improvements
  Find correct region of interest and have cut off based system
  Parallelize the execution of Zsim+bookism
A more aggressive VC allocation implementation for the router
Identify the ideal phaselength to further improve on the simulation time without compromising on the accuracy.
Extract traffic pattern of to identify possible sources of congestion in network links
Implement PInternet for other networks like crossbar and butterfly
Using the pagerank traffic results and traffic pattern to understand the shortcoming of the current workload which will be used to identify better workloads for future work
  run set of workloads with non-uniform access pattern and test network performance with different injection rate and traffic pattern