## Slide 1: Learning gem5
Jason Lowe-Power
http://www.lowepower.com/jason/learning_gem5/

## Slide 2: What is gem5?
Michigan m5 + Wisconsin GEMS = gem5
“The gem5 simulator is a modular platform for computer-system architecture research, encompassing system-level architecture as well as processor microarchitecture.”
Nathan Binkert, Bradford Beckmann, Gabriel Black, Steven K. Reinhardt, Ali Saidi, Arkaprava Basu, Joel Hestness, Derek R. Hower, Tushar Krishna, Somayeh Sardashti, Rathijit Sen, Korey Sewell, Muhammad Shoaib, Nilay Vaish, Mark D. Hill, and David A. Wood. 2011. The gem5 simulator. SIGARCH Comput. Archit. News 39, 2 (August 2011), 1-7. DOI=http://dx.doi.org/10.1145/2024716.2024718

## Slide 3: This tutorial
This is going to interactive
Work along with me for best results
Ask questions!!

## Slide 4: Schedule
Learning Part I 8:30 – 10:00
Break 10:00 – 10:30
Learning Part II 10:30 – 12:00
Lunch 12:00 – 1:30
Code Sprint I 1:30 – 3:00
Break 3:00 – 3:30
Code Sprint II 3:30 – 5:00
Code Sprint II:
Continue sprints!
Learning Part II:
Event-driven simulation
SimObject parameters
Memory system objects
Other gem5 features
Learning Part I:
Building gem5
Config scripts
gem5 output
Simple SimObject
Code Sprint I:
New gem5 contributions [Andreas Sandberg]
Begin sprints!

## Slide 5: Building gem5
http://learning.gem5.org/book/part1/building.html

## Slide 6: Let’s get started!
Switch!
> git clone https://gem5.googlesource.com/public/gem5
> cd gem5
> scons build/X86/gem5.opt –j5
and now we wait (about 8 minutes)

## Slide 7
> scons build/X86/gem5.opt –j5
scons: the build system that gem5 uses (like make). See http://scons.org/
build/X86/gem5.opt: “parameter” passed to scons. gem5’s Sconscript interprets this. Also, the patch to the gem5 executable.
X86: Specifies the default build options. See build_opts/*
opt: version of executable to compile (one of debug, opt, perf, fast)
Notes: You may want to build debug if you have < 8GB of memory.

## Slide 8: gem5 architecture
gem5 consists of “SimObjects”
Most C++ objects in gem5 inherit from class SimObject
Represent physical system components

## Slide 9: gem5 architecture
gem5 is a discrete event simulator
Event at head dequeued
Event executed
More events queued
Event - 10
Event Queue
Event - 11
Event - 20
Event - 50
Event - 50
Event - 52
Event - 55
All SimObjects can enqueue events to the event queue
We’ll cover more after the break

## Slide 10: gem5 configuration scripts
http://learning.gem5.org/book/part1/simple_config.html
http://learning.gem5.org/book/part1/cache_config.html

## Slide 11: gem5 user interface
gem5 completely controlled by Python scripts
Scripts define system to model
All (C++) SimObjects exposed to Python
So… let’s make one!

## Slide 12: Simple config script
Single CPU connected to a memory bus
Switch!

## Slide 13: Simple config script
http://learning.gem5.org/book/_downloads/simple.py

## Slide 14: Running gem5
> build/X86/gem5.opt configs/myscripts/simple.py
build/X86/gem5.opt: the gem5 binary to run
configs/…/simple.py: the configuration script (config script)

## Slide 15: Port interface
| system.cpu.icache_port = system.membus.slave
| system.cpu.dcache_port = system.membus.slave
| ...
| system.mem_ctrl.port = system.membus.master
Ports connect MemObjects
Master
Slave
Requests
Responses
To register a connection between master and slave, use ‘=’ in Python

## Slide 16: Syscall Emulation (SE) mode
| process = LiveProcess()
| process.cmd = [‘tests/.../hello’]
| system.cpu.workload = process
| ...
| root = Root(full_system = False)
SE mode emulates the operating system (Linux) syscalls. No OS runs.
process: an emulated process with emulated page tables, file descriptors, etc.
Full system mode runs a full OS as if gem5 is a “bare metal” system. Like full virtualization.

## Slide 17: Going further: Adding caches
Extending SimObjects in Python config
Object-oriented config files
Adding command-line parameters
http://learning.gem5.org/book/part1/cache_config.html
Switch!

## Slide 18: It’s just Python!
| class L1Cache(Cache):
| ...
|
| class L1ICache(L1Cache):
| def connectCPU(self, cpu):
| self.cpu_side = cpu.icache_port
| ...
Use good object-oriented design!
Debugging config files is easy. Just add some print statements!
Use Python builtins to provide support for command line parameters.
See text for details

## Slide 19: Understanding gem5 output
http://learning.gem5.org/book/part1/gem5_stats.html

## Slide 20: Understanding gem5 output
> ls m5out
config.ini config.json stats.txt
config.ini: Dumps all of the parameters of all SimObjects.
This shows exactly what you simulated.
config.json: Same as config.ini, but in json format.
stats.txt: Detailed statistic output. Each SimObject defines and updates statistics. They are printed here at the end of simulation.

## Slide 21: stats.txt
Switch!
---------- Begin Simulation Statistics ----------
sim_seconds 0.000346 # Number of seconds simulated
sim_ticks 345518000 # Number of ticks simulated
final_tick 345518000 # Number of ticks from beginning ...
sim_freq 1000000000000 # Frequency of simulated ticks
...
sim_insts 5712 # Number of instructions simulated
sim_ops 10314 # Number of ops (including micro ...
...
system.mem_ctrl.bytes_read::cpu.inst 58264 # Number of bytes ...
system.mem_ctrl.bytes_read::cpu.data 7167 # Number of bytes ...
...
system.cpu.committedOps 10314 # Number of ops (...
system.cpu.num_int_alu_accesses 10205 # Number of integer ...
sim_seconds: name of stat. This shows simulated guest time
Every SimObject can have its own stats. Names are what you used in the Python config file

## Slide 22: A simple SimObject
http://learning.gem5.org/book/part2/helloobject.html

## Slide 23: gem5’s coding guidelines
Follow the style guide (http://www.gem5.org/Coding_Style)
Install the style guide when scons asks
Don’t ignore style errors
Use good development practices
<Add something here about git branches?>

## Slide 24: Adding a new SimObject
Step 1: Create a Python class
Step 2: Implement the C++
Step 3: Register the SimObject and C++ file
Step 4: (Re-)build gem5
Step 5: Create a config script
Switch!

## Slide 25: Step 1: Create a Python class
| from m5.params import *
| from m5.SimObject import SimObject
|
| class HelloObject(SimObject):
| type = ‘HelloObject’
| cxx_header = ‘learning_gem5/hello_object.hh’
Import the objects we need
m5.params: Things like MemorySize, Int, etc.
type: The C++ class name
cxx_header: The filename for the C++ header file
HelloObject.py

## Slide 26: Step 2: Implement the C++
| #include "params/HelloObject.hh"
| #include "sim/sim_object.hh"
| class HelloObject : public SimObject
| {
| public:
| HelloObject(HelloObjectParams *p);
| };
hello_object.hh
params/*.hh generated automatically. Comes from Python SimObject definition
Constructor has one parameter, the generated params object.

## Slide 27: Step 2: Implement the C++
HelloObject::HelloObject(HelloObjectParams *params) : SimObject(params)
{
std::cout << "Hello World! From a SimObject!" << std::endl;
}
HelloObject*
HelloObjectParams::create()
{
return new HelloObject(this);
}
hello_object.cc
HelloObjectParams: when you specify a Param in the Hello.py file, it will be a member of this object.
You must define this function (you’ll get a linker error otherewise). This is how Python config creates the C++ object.

## Slide 28: Step 3: Register the SimObject and C++ file
| Import(*)
| SimObject(‘Hello.py’)
| Source(‘hello_object.cc’)
SConscript
Import: SConscript is just Python… but weird.
SimObject(): Says that this Python file contains a SimObject. Note: you can put pretty much any Python in here
Source(): Tell scons to compile this file (e.g., with g++).

## Slide 29: Step 4: (Re-)build gem5

## Slide 30: Step 5: Create a config script
| ...
| system.hello = HelloObject()
| ...
Instantiate the new object that you created in the config file (e.g., simple.py)
> build/X86/gem5.opt configs/learning_gem5/hello.py
...
Hello world! From a SimObject!
...

## Slide 31: Simple SimObject code
http://learning.gem5.org/book/_downloads/HelloObject.py
http://learning.gem5.org/book/_downloads/hello_object.hh
http://learning.gem5.org/book/_downloads/hello_object.cc
http://learning.gem5.org/book/_downloads/SConscript
http://learning.gem5.org/book/_downloads/run_hello.py

## Slide 32: Debug support in gem5
http://learning.gem5.org/book/part2/debugging.html

## Slide 33: Adding debug flags
Switch!
DebugFlag(‘Hello’)
DPRINTF(Hello, “Created the hello object”);
Declare the flag: add the debug flag to the SConscript file in the current directory
DPRINTF: macro for debug statements in gem5
Hello: the debug flag declared in the SConscript.
Found in “debug/hello.hh”
Debug string: Any C format string
SConscript
hello_object.cc

## Slide 34: Debugging gem5
Switch!
> build/X86/gem5.opt --debug-flags=Hello configs/learning_gem5/hello.py
...
0: system.hello: Hello world! From a debug statement
debug-flags: Comma separated list of flags to enable. Other options include --debug-start=<tick>, --debug-ignore=<simobj name>,
etc. See gem5.opt --help

## Slide 35: Event-driven programming
http://learning.gem5.org/book/part2/events.html

## Slide 36: Simple event callback
Switch!
| class HelloObject : public SimObject
| {
| private:
| ...
| void processEvent();
| EventWrapper<HelloObject,
| &HelloObject::processEvent> event;
| public:
| HelloObject(HelloObjectParams *p);
| void startup();
| };
EventWrapper: Convenience class for simple events with no parameters.
processEvent: Callback function to run when event fires.
startup: Called after all SimObjects instantiated. Schedule local events here.

## Slide 37: Simple event callback
Switch!
| void
| HelloObject::processEvent()
| {
| timesLeft--;
| DPRINTF(Hello, "Hello world!"
| " Processing the event! %d left\n", timesLeft);
| if (timesLeft <= 0) {
| DPRINTF(Hello, "Done firing!\n");
| } else {
| schedule(event, curTick() + latency);
| }
| }
schedule: Put an event instance on the event queue. An absolute tick used for when the event is processed.
curTick: Returns the current simulator time. Useful for relative time computations.

## Slide 38: Event SimObject code
http://learning.gem5.org/book/_downloads/hello_object1.hh
http://learning.gem5.org/book/_downloads/hello_object2.cc

## Slide 39: SimObject parameters
http://learning.gem5.org/book/part2/parameters.html

## Slide 40: Adding parameters
Switch!
| class HelloObject(SimObject):
| type = 'HelloObject'
| cxx_header = "learning_gem5/hello_object.hh"
|
| time_to_wait = Param.Latency("Time before firing the event")
| number_of_fires = Param.Int(1, "Number of times to fire the event before "
| "goodbye")
Param.<TYPE>: Specifies a parameter of type <TYPE> for the SimObject
Param.<TYPE>(): First parameter: default value. Second parameter:

## Slide 41: Going further: More parameters
Included types (e.g., MemorySize, MemoryBandwidth, Latency)
Using a SimObject as a parameter
SimObject-SimObject interaction
http://learning.gem5.org/book/part2/parameters.html

## Slide 42: MemObjects
http://learning.gem5.org/book/part2/memoryobject.html

## Slide 43: MemObject
Object that is part of gem5’s memory system
both classic caches and Ruby are MemObjects
Allowed to have MasterPorts and SlavePorts

## Slide 44: Packets
Unit of transfer between MemObjects
Packets pass between Master and Slave ports
Packets have
Request
Command
Data
Much more…

## Slide 45: Master and slave ports
Master
Slave
sendTimingReq
recvTimingReq
returns: true
Slave executes request
Time
sendTimingReq: send a Packet containing a request from a master to a slave
recvTimingReq: function that is called to handle the request in the slave port.
return true: The slave can handle the request.

## Slide 46: Master and slave ports
Master
Slave
sendTimingReq
recvTimingReq
returns: true
returns: true
Slave executes request
recvTimingResp
sendTimingResp
Time
sendTimingResp: The slave finishes processing the request, and now sends a response (same packet).
recvTimingResp: Handles the response from the slave. Returning true means the packet is handled.

## Slide 47: Master and slave ports
Master
Slave
sendTimingReq
recvTimingReq
returns: false
Slave busy
Time
sendTimingReq
recvTimingReq
returns: true
recvReqRetry
sendReqRetry
return false: Slave cannot currently process the Packet. Resend the packet later. The Master’s responsibility to track Packet.
sendReqRetry: Tell the master it can retry the stalled Packet.
recvReqRetry: Can now retry the request by calling sendTimingReq.

## Slide 48: Master and slave ports
Master
Slave
Master busy
returns: false
recvTimingResp
sendTimingResp
return false: Master cannot currently process the Packet. Resend the packet later. The Slave’s responsibility to track Packet.
returns: true
recvTimingResp
sendTimingResp
sendRespRetry
recvRespRetry
sendRespRetry: Slave can now retry the response.

## Slide 49: Master and slave port interface
Master
recv​‌ Timing Resp
recv Req Retry
recv Range Change
Slave
recv Timing Req
recv Resp Retry
recv Functional
get Addr Ranges

## Slide 50: Simple MemObject
Switch!

## Slide 51: Going further: Implementing a cache
Full implementation of a uniprocessor cache (no coherence support)
Emulation concepts (using STL for associative data)
Vector ports, clocked objects, upgrading and creating packets
http://learning.gem5.org/book/part2/simplecache.html

## Slide 52: Other gem5 concepts
A random assortment

## Slide 53: ISA support
gem5 supports many ISA
ARM: ARM Research often contributes
x86: Very complicated, there are a few bugs
RISC-V: Recent contribution. SE mode working. Thanks Alec!
Alpha, MIPS, SPARC, Power: No maintainers. Not very supported.

## Slide 54: CPU Models
gem5 exposes a flexible CPU interface
AtomicSimpleCPU: No timing. Fast-forwarding & cache warming.
TimingSimpleCPU: Single-cycle (IPC=1) except for memory ops.
O3CPU: Out-of-order model. Highly configurable.
MinorCPU: In-order model (not fully tested with x86)

## Slide 55: Full system support
Full system is like a virtual machine.
gem5 exposes a “bare metal” interface
Requires a kernel, disk image, etc.
See http://learning.gem5.org/book/part3/ for simple x86 example

## Slide 56: Coherence modeling (Ruby)
“Classic cache” vs. Ruby
Classic: MOESI only, Ruby: any protocol
Classic: Hierarchical-snooping, Ruby: Snooping or directory or…
Classic: Flexible hierarchy, Ruby: Hierarchy baked into protocol
Classic: Good baseline CMP, Ruby: Required for coherence study
Ruby protocols in src/mem/protocols
SLICC is a DSL for coherence
Not much documentation, but many examples!
Very flexible network simulation (Garnet)

## Slide 57: GPU and device models
AMD recently released a HSAIL GPU model (src/gpu-compute)
Many devices supported for FS simulation
Ethernet (and multi-system simulation)
VNC for graphics
IDE controllers for disks
Most devices are functional-only

## Slide 58: Other features
Probes and tracing
Remote GDB
Dynamically-linked binaries in SE mode
Power modeling
And many, many, many others

## Slide 59: Caveats
gem5 is a tool, not a panacea
Most models are not validated against “real” hardware
See “Architectural Simulators Considered Harmful” https://doi.org/10.1109/MM.2015.74
There are bugs!

## Slide 60: Getting (more) help
Main gem5 wiki: http://gem5.org/
My book:
  Learning.gem5.org
  https://github.com/powerjg/learning_gem5
Mailing lists: http://gem5.org/Mailing_Lists
  gem5-users: General user questions (you probably want this one)
  gem5-dev: Mostly code reviews and high-level dev talk
gem5 QA (like StackOverflow): http://qa.gem5.org/

## Slide 61: Backup slides
Mostly from other versions of this tutorial

## Slide 62: Adding caches
The previous example was boring
Let’s add some caches!
Switch!

## Slide 63
| from m5.params import *
|...
|
| class BaseCache(MemObject):
| type = ‘BaseCache’
| abstract = True
| cxx_header = ‘mem/cache/base.hh’
|
| size = Param.MemorySize(“Capacity”)
| assoc = Param.Unsigned(“Associativity”)
| ...
| tags = Param.BaseTags(LRU(), “Tag ...”)
| ...
| cpu_side = SlavePort(“Upstream port...”)
| mem_side = MasterPort(“Downstream...”)
| ...
| class Cache(BaseCache):
| type = ‘Cache’
| cxx_header = ‘mem/cache/cache.hh’
| ...
Definition of a SimObject
The C++ class for the SimObject. And it’s header file.
size: A parameter to the SimObject, of type MemorySize.
No default, so it is required in Python config file
tags: A parameter of type BaseTags (another SimObject).
There is a default, so it is not required in Python config file

## Slide 64
| from m5.params import *
|...
|
| class BaseCache(MemObject):
| type = ‘BaseCache’
| abstract = True
| cxx_header = ‘mem/cache/base.hh’
|
| size = Param.MemorySize(“Capacity”)
| assoc = Param.Unsigned(“Associativity”)
| ...
| tags = Param.BaseTags(LRU(), “Tag ...”)
| ...
| cpu_side = SlavePort(“Upstream port...”)
| mem_side = MasterPort(“Downstream...”)
| ...
| class Cache(BaseCache):
| type = ‘Cache’
| cxx_header = ‘mem/cache/cache.hh’
| ...
Ports that connect the cache to the memory system. Again, masters send requests, slaves receive requests,.
These cannot have defaults. Must specify the sender/receiver in Python config files.
Switch!

## Slide 65: Cache scripts
http://learning.gem5.org/book/_downloads/caches.py
http://learning.gem5.org/book/_downloads/two_level.py

## Slide 66: Architectural exploration
> build/X86/gem5.opt configs/learning_gem5/part1/two_level.py
...
Exiting @ tick 56435000 because target called exit()
> build/X86/gem5.opt configs/learning_gem5/part1/two_level.py
...
Exiting @ tick 30896000 because target called exit()
> build/X86/gem5.opt configs/learning_gem5/part1/two_level.py
--l1d_size=4kB
Exiting @ tick 30943000 because target called exit()
| ...
| system.cpu = TimingSimpleCPU()
| ...
|
| ...
| # system.cpu = TimingSimpleCPU()
| system.cpu = DerivO3CPU()
|
| ...
| # system.cpu = TimingSimpleCPU()
| # system.cpu = DerivO3CPU()
| system.cpu = MinorCPU()
DerivO3CPU: gem5’s out-of-order model
MinorCPU: gem5’s in-order model
SimpleTiming | 56435000
DerivO3 | 30896000
4 kB L1 | 30943000

## Slide 67: Next time…
How to make changes to gem5
Adding new SimObjects
What’s in gem5
Let me know (powerjg@cs.wisc.edu) anything specific to cover!

## Slide 68
Switch!
> hg clone http://repo.gem5.org
> cd gem5
> scons build/X86/gem5.opt –j5
scons: the build system that gem5 uses (like make). See http://scons.org/